## Slide 1: Progress of Injector Linac
Kazuro Furukawa
for Injector Linac

## Slide 2: Mission of electron/positron Injector in SuperKEKB
40-times higher Luminosity
  Twice larger storage beam  Higher beam current at Linac
  20-times higher collision rate with nano-beam scheme
     Low-emittance even at first turn  Low-emittance beam from Linac
     Shorter storage lifetime  Higher Linac beam current
Linac challenges
  Low emittance e-
    with high-charge RF-gun
  Low emittance e+
    with damping ring
  Higher e+ beam current
    with new capture section
  Emittance preservation
    with precise beam control
  4+1 ring simultaneous injection
Linac Overview
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Injector Linac Operational History
Chart: FY
| 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0
Operation Time / year [hrs] | 2100 | 2100 | 2800 | 2824 | 3443 | 4487 | 5110 | 4542 | 5303 | 5234 | 5117 | 5299 | 5070 | 4563 | 4123 | 3828 | 5906 | 7297 | 7203 | 7239 | 7086 | 6815 | 7117 | 6988 | 6927 | 6322 | 6556 | 6362 | 5847 | 5492 | 5331 | 5315
Total Operation Time [hrs] | 210 | 420 | 700 | 982.4 | 1326.7 | 1775.4 | 2286.4 | 2740.6 | 3270.9 | 3794.3 | 4306 | 4835.9 | 5342.9 | 5799.2 | 6211.5 | 6594.3 | 7184.9 | 7914.6 | 8634.9 | 9358.8 | 10067.4 | 10748.9 | 11460.6 | 12159.4 | 12852.1 | 13484.3 | 14139.9 | 14776.1 | 15360.8 | 15910 | 16443.1 | 16974.6
Machine Failure [%] | 0.74 | 0.37 | 3.9 | 4.6 | 1.3 | 1.7 | 2 | 1.4 | 0.9 | 0.8 | 0.7 | 0.6 | 2.9 | 7.1 | 7.4 | 6.5 | 4.3 | 2.9 | 3.7 | 1.8 | 1.2 | 1.37 | 1.9 | 1.78 | 1.7 | 1.52 | 1.06 | 1.29 | 0.43

## Slide 4: Operation Statistics
FY2013 Statistics
  Operation time: 5315 hours (FY2012 -0.3%)
    PF/PF-AR Injection and Commissioning for SuperKEKB
  Failure rate: 0.43% (FY2012 -0.87 point)
    Failures include stand-by devices
    Not all of failures affected the injections
  Failure rate was the best in these 20 years
    Earthquake recovery goes well
    Old devices do not reach their lifetimes yet
    Commissioning for SuperKEKB is performed deliberately

## Slide 5: Positron Generation
4-times more positron is required at SuperKEKB than KEKB
  Safety measure was taken after cable fire during the test of Flux Concentrator (FC)
  New components in 100-m capture section were tested in steps
  High voltage tests in tunnel in April
  Beam tests with electron in May

## Slide 6: Positron generation for SuperKEKB
New positron capture section after target with Flux concentrator (FC) and large-aperture S-band structure (LAS)
Satellite bunch (beam loss) elimination with velocity bunching
Pinhole (2mm) for electrons beside target (3.5mm)
Beam spoiler for target protection
Flux
Concentrator
e+
5 nC injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulsed ST
DC QM
pulsed QM
side view
spoiler
solenoid
LAS Accel.
structure
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
e+ beam

## Slide 7: Flux Concentrator (FC)
外周の一次コイルにパルス電流を流して導体内に誘導電流を発生させると、磁束(flux)が開口部内に圧縮(concentrate)され強いソレノイド磁場ができる。
FC | parameters
length | 100 mm
outer diameter | 100 mm
inner diameter (min.) | 7 mm
inner diameter (max.) | 52 mm
peak current | 12 kA
pulse width | 6 ms (half-sine)
peak field | 3.5 T
inductance | 1.0 mH
T.Kamitani

## Slide 8: 陽電子生成標的
標的材料 タングステン 14 mm長 (= 4.0 X0)
タングステンと銅の胴体はHIP加工で接合
標的内の熱分布
標的
ビーム通過孔
tungsten
beam hole
flux
concentrator
return
yoke
T.Kamitani

## Slide 9: 標的破壊防止用 Beam spoiler
screen & scatterer
target
hole
injection
e- beam
primary e-
e+
hole
spot size
camera
target上でのbeam spot sizeを sx ,sy> 0.7 mm に拡げてpeak energy密度を下げ、破壊を防ぐ
スクリーン兼用 Al2O3 板 (0.14 mm thick) + Al 散乱板 (0.25 mm thick) [総物質量 = 0.05 X0]
spoiler上にも beam hole 有り
3m distance
Front
Rear
T.Kamitani

## Slide 10: 陽電子捕獲部 (e+ capture section)
KLY
1-5
KLY
1-6
SLED
SLED
LAS加速管
LAS
加速管
DC solenoid
LAS : Large Aperture S-band 加速管
開口直径30mm：通常の 1.5倍
LAS 10 MV/m [SLED off]
減速位相capture &
RF位相スリップ &加速位相に乗る
LAS 12 MV/m [SLED on]
加速位相
Solenoids: FC_16_21
Solenoids: FC_15_11
FC:
FL_15_T
BC:
FC_15_T
T.Kamitani

## Slide 11: 陽電子捕獲部@Linacトンネル
この中にFC、標的
ブリッジコイルが
収められている。
電子ビーム
2014年4月に陽電子捕獲部
をビームラインの設置し、
5月より陽電子のコミッショニング
を開始した。
DCソレノイド
T.Kamitani

## Slide 12: 電子陽電子セパレータ
FCの広いアクセプタンスのため 捕獲部の出口まで、陽電子とほぼ等量 の二次電子がやってくる
ビーム位置モニターの信号が電子と陽電子 で混ざってしまい正しい情報が得られない
二次電子はシケイン中のストッパブロックで 止め、陽電子のみ通す。
入射電子ビームは真ん中を通る。
二次電子ストッパーブロック
入射電子ビーム
陽電子ビーム
二次電子ビーム
bending
magnet
T.Kamitani

## Slide 13: Qマグネット収束系
64mの領域にわたって、
加速管のレイアウトを変更し
Qマグネットを増設して
アクセプタンスを拡張した。
T.Kamitani

## Slide 14: First Positron Observation from New Generator
Devices and primary electron beam studied
First positron signal confirmed on Jun.5
Positrons transferred to the beam dump on Jun.6
Consistent with simulation designs
Expect design achievement after full constructions
Signal from primary electron
Signal from positron with opposite polarity

## Slide 15: Positron from New Positron Capture Section
Generated positron ~0.1nC was transferred to the entrance of damping ring
With higher magnetic and electric field, 4-nC positron will be generated
Target shield (40cm x 6m long) will be finalized
Alignment will be improved 3mm  0.1mm
Horizontal
400 m
Vertical
Beam charge
Primary Electron
Beam position
Positron
W target
~0.1 nC
Flux concentrator and
following solenoid/quad
Large aperture S-band structure before solenoid & quad installation

## Slide 16: (1) FC current
6kAより大きな電流値でもまだ saturationせずに順調に伸びていくと 期待される
新型電源では12kAまで上がる予定。
snubber回路無しではさらに上がる
可能性あり。
FC currentがzeroでも
ある程度のyieldがある
CT測定値
FCでの実電流値は1.07倍
plot上の6kA => 6.42 kA
T.Kamitani

## Slide 17: (2) Bridge Coil current
[1] 650A以上ではほぼ一定。
電源最大値は750A。現在はケーブルの
発熱より600A以下で運転している
なお、FC currentに比べて最大到達値
が低いのは、このデータの方が早い
時期に取られたがその後チューニング
によりyieldが向上したためである。
[2] zero currentではyieldが低い。
T.Kamitani

## Slide 18: (3) DC solenoid 1-5 current
Yieldがややsaturationの傾向？
FC currentが高くなるとこれも もっと向上するかもしれない
本来の電源最大値は650Aであるが
電力系の制約より370A以下で運転
している。2014年秋以降改善予定
現在のBPMでは0.02nC以下は
backgroundに埋もれて測れないので
yieldも0.06以下はfakeのゲタ。
T.Kamitani

## Slide 19: (4) DC solenoid 1-6 current
320A付近がoptimumでそれより
上では悪化する
FC currentが高くなるとこれも もっと向上するかもしれない
本来の電源最大値は650Aであるが
電力系の制約より370A以下で運転
している。2014年秋以降改善予定
T.Kamitani

## Slide 20: (5) e+ RF phase [1-5と1-6の位相関係は固定]
減速捕獲
加速捕獲
FCの広いアクセプタンスのおかげで減速捕獲でもほぼ同じ収量が得られる。
減速捕獲の方が陽電子のバンチ長、エネルギー広がりが小さい。
シミュレーションに比べて絶対値には
すこしズレがあるが位相依存性について
はよく再現されている。
測定値
simulation
T.Kamitani

## Slide 21: (6) Acc-field grad./phase at 1-5
T.Kamitani

## Slide 22: (6-2) Acc-field grad. [MV/m] at 1-5
SLED を使用し、14MV/m 程度まで向上する予定
T.Kamitani

## Slide 23: Positron Generation
Installation of positron generator for SuperKEKB in April 2014 (Beamline construction since summer 2013) (positron target, spoiler, Flux Concentrator, bridge coils, LAS structures [x6], DC solenoids [16+13], e+/e- separator, quads [>90])
Commissioning of positron beam, observation of the first positron after reconstruction for SuperKEKB, further improvements expected
Oct.~Dec.2014 : Linac commissioning Jan.~Mar.2015 : Construction Apr.~Jun. : Linac commissioning Jul.~Sep.2015 : Construction Oct. : LER injection
T.Kamitani
 | Primary e- [nC] | Positron [nC] | Efficiency | Parameters
June 2014 | 0.6 | 0.12 | 20% | FC 6.4kA, Solenoids 370A, LAS capture field 10 MV/m
Specification (at SY2) | 10.0 | 5.0 | 50% | FC 12kA, Solenoids 650A, LAS capture field 14 MV/m
DR injection (2016?) |  | 4.0 | 40% | Energy spread acceptance 0.5%
x17
x42
x2.5

## Slide 24: Facility for Electric Power and Cooling Water
4.0 GeV e+
4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
SuperKEKB injector
e+ target &
LAS capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
AR
6.5 GeV e-
3T
RF gun
[1] Sector 1,2
Electricity and cooling water addition for new positron generator
+920 kVA, +900 L/min
[2] Sector 2,3
Electricity addition for new damping ring
+310 kVA
[3] Sector 5
Electricity and cooling water addition for energy compression, beam diag., injection beamlines
+300 kVA, +460L/min
Linac needs electricity and cooling water extensions, especially for positron generator upgrade, that was planned in FY2012
Separate building construction in FY2013 not to impact PF/PF-AR
Facility extensions performed during summer 2014

## Slide 25: Photo cathode RF gun development
5.6 nC / bunch was confirmed
Next step: 50-Hz beam generation & Radiation control
Quasi traveling wave side couple cavity
Cascaded frequency doublers
Yb fiber and Yb:YAG think disk laser
Ir5Ce photo cathode
Ir5Ce Cathode

## Slide 26: Photo cathode RF gun improvement
Crucial for high-current low-emmittance beam
New Ir5Ce cathode and new cavity QTWSC were successful
Basic features were confirmed at 2 ~ 5 Hz
Expect beam parameter and stability performance at 50 Hz
Staged laser system improvements with beam measurements
Regenerative amplifiers were replaced with multi-pass amplifiers for their heat to achieve 25 Hz then 50 Hz

## Slide 27: Emittance Preservation and Alignment
If Device is off center of the beam
  Focusing magnet (quad) kicks the beam bunch
  Accelerating structure (cavity) excites wakefield, to bend the tail
Distorted bunch in banana shape
  Emittance dilution or blow-up, even 100 times larger
    Depending on the beam optics and the beam charge
Alignment and orbit correction is crucial to preserve the emittance
Focusing Magnet
Beam
Accelerating Structure
Transverse beam distribution in time direction
Sugimoto et al.

## Slide 28: Emittance Preservation
Offset injection may solve the issue
Orbit have to be maintained precisely
Mis-alignment should be <0.1mm locally, <0.3mm globally
100 samples
Mis-alignment leads to Emittance blow-up
Sugimoto et al.
Orbit manipulation compensates it

## Slide 29: Alignment
High-precision alignment was not necessary in PF and KEKB injections, and it was much damaged by earthquake in 2011.
Instead of flexible-structure girder before earthquake, rigid-structure was adopted with jack-volts and fixed supports.
Reflector pedestals are mounted onto quad magnets and accelerating cavities for laser-tracker measurement.
Iterative measurement and adjustment with 500-m straight laser and position sensors should enable 0.3-mm global alignment.
Laser tracker should enable 0.1-mm measurement within 10-m girder unit.
Displacement gauges, hydrostatic leveling, inclinometer are also employed.
Remote measurement system and girder mover system will be necessary for longer term, and are under development.

## Slide 30: Alignment work at summer 2014
For the first time at 3-5 sectors
Horizontal axis: sensor number from sector C, 1-4, to sector 5 (~80 m/sector)
Vertical axis: voltage (~displacement at 0.25~0.5mm/V)
Some girders were not yet upgraded
Moved up to 3 mm not to break vaccuum

## Slide 31: Alignment work during summer 2014
Several measurements during summer
Measurement reproducibility was confirmed up to ~0.2 mm
While there existed many conflicting measurements, consistent scheme has been established
Movement of tunnel by several 10’s of micrometer was observed (→ mover)

## Slide 32: Instrumentation
RF stability is crucial for the beam
  LLRF monitor is being developed
  60 high-power klystrons and 10 middle-power systems
  50Hz synchronized data acquisition with event (beam-mode) recognition
  0.1% amplitude and 0.1degree phase resolution
BPM precision improvement
  100μm  50μm  < 10μm
  Event recognition
  Mass production is underway
Other beam monitors

## Slide 33: Staged Radiation Control License towards SuperKEKB
Two licenses were approved in June 2014
[1] Beam diagnostic station at #A2 just after gun
  for 1250nC/s at 50Hz 2bunches
[2] Beam dump at #28 just before damping ring
  for 10nC/s with positrons
Radiation measurements especially at positron generator
  Indispensable to estimate radiation at >100 times higher beam
Both approved
Soon apply for the next license at ~May.2015

## Slide 34: Linac Schedule Overview (as of Mar.2014)
RF-Gun e- beam
commissioning
at A,B-sector
Qe- = 5nC
e- commiss.
at A,B,J,C,1
Qe- = 5nC
e+ commiss.
at 1,2 Qe+ = 0.5nC (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 Qe- = 5nC
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~5nC
PF-AR e-
commiss.
: Electron
: Positron
: Low current electron
2 nC
4 nC
1 nC

## Slide 35: Linac Schedule Overview (Newer)
RF-Gun e- beam
commissioning
at A,B-sector
Qe- = 5nC
e- commiss.
at A,B,J,C,1
Qe- = 5nC
e+ commiss.
at 1,2 Qe+ = 0.5nC (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 Qe- = 5nC
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~5nC
PF-AR e-
commiss.
: Electron
: Positron
: Low current electron
2 nC
4 nC
1 nC

## Slide 36: Summary
Steady progress towards first MR injection in 2015
Will finish earthquake disaster recovery in 2014
Will make staged improvements before 2017
Will balance between final beam quality and stable/staged operation
Will select optimized route depending on available resources

## Slide 37
SuperKEKB
dual rings
Mt. Tsukuba
Injector Linac
PF-AR
PF
Thank you

## Slide 40: Positron Source
High current positron is required
Positron capturing with flux concentrator (FC) and large aperture s-band structure (LAS)
Deceleration field to reduce satellite bunches
Pinhole beside target for electron beam
Protection system with beam spoilers

## Slide 41: Positron beamline under construction
KLY
1-5
KLY
1-6
SLED
SLED
LAS 14 MV/m
deceleration & phase slip & acceleration
LAS 10 MV/m
acceleration
Solenoids
target
+FC
primary e- 3.2 GeV, 10 nC x 2 bunch, 50 Hz
tungsten target
AMD system (5.0 T x 200mm + 0.4 T x 15m) Flux Concentrator DC solenoids
KLY1 2m LAS x 2 (14 MV/m), aperture 2a = 32 -> 30 mm (typical S-band ~20 mm)
KLY2 2m LAS x 4 (10 MV/m), aperture 2a = 32 -> 30 mm
e+ beam energy at capture section exit : 110 MeV
e+ yield: N(e+)/N(e-) = 49 % at 1.1 GeV DR
Deceleration capture
LAS : Large Aperture S-band structure

## Slide 42: Flux Concentrator Assembly
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
e+ beam
quick detachable power & water connection
to minimize worker's radiation dose
FC assembly

## Slide 43: e+/e- beam switching at target
Flux
Concentrator
e+
5 nC injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulse ST
DC QM
pulse QM
side view
rear view
e+ on-axis, e- offset -> e- emittance growth by solenoid kick induced orbit
e- on-axis, e+ offset -> e+ yield degradation (50% -> 20%)
target
offset
3.5 mm
2.0 mm
FC offset
7.0 mm
FC aperture
spoiler
target
diameter
4.0 mm
hole
diameter
2.0 mm
solenoid
LAS Accel.
structure
we take this scheme.
Two possible schemes of beam switching by orbit bump
T.Kamitani

## Slide 44: Energy profiles and beam properties
low emittance
RF gun
A
B
C
1
2
3
4
5
1.5 GeV e-
e+ target
e-:Chicane
10 nC x 2 (for LER)
5 nC x 2 (for HER)
0.3 nC x 1 (for AR)
0.3 nC x 1 (for PF)
1.1 GeV
DR
Decelerate
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
same energy
e-/e+ beams are delivered to 4-rings with different current & energy.
Beam acceleration modes must be switched by 50 Hz pulse-by-pulse for top-up injection.
Beam optics should satisfy the fast beam-mode switching.
HER: 7 GeV e-
AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 2.5 GeV e+
5 nC x2
0.3 nC x1
0.3 nC x1
4 nC x2

## Slide 45: Pulse-to-pulse modulation
ARC
e– (2.5GeV, 0.2nC)
e− Gun
ARC
e+ Target
e+ (4GeV, 4nC)
e− Gun
PF Injection
SuperKEKB-LER Injection
e– (3.5GeV, 10nC)
ARC
e– (7GeV, 5nC)
e− Gun
SuperKEKB-HER Injection
ARC
e– (6.5GeV, 5nC)
e− Gun
PF-AR Injection
Damping ring
Event-based Control System
Every 20 ms
F.B
F.B
F.B
F.B
F.B
F.B
F.B
F.B
Four PPM virtual accelerators for SuperKEKB project maybe with additional PPM VAs for stealth beam measurements based on Dual-tier controls with EPICS and event-system