## Slide 1: Injector upgrade
23 Oct. 2015
Toshi Higo (on behalf of Injector linac group)

## Slide 2: Contents
Beam requirement
Schedule and upgrade scenario
Positron status and near future plan
Emittance related issues
Conclusion

## Slide 3: SuperKEKB schedule
Commissioning is divided into three stages.
(phase1, phase2, phase3)
2018
2015
2016
2017
Calendar
Power restriction
in summer
Power restriction
in summer
Power restriction
in summer
Power restriction
in summer
Phase 1
Phase 2
QCS, Belle II install
VXD install
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
Phase 3
w/ full Belle II
DR commissioning
w/ DR
Vacuum Scrubbing
Basic machine tuning
Current=1A
Full Current
L= 11034cm-2s-1
(KEKB design)
L= 81035cm-2s-1
Current plan on going
w/ DR
w/o DR
low emittance
low emittance
4~5 nC/bunch
2 nC/bunch
1 nC/bunch
Injection Beam
no Top-up inj.
Top-up injection
Top-up injection
Add more RF
Based on Miura-Furukawa, B2GM in June 2015
Linac

## Slide 4: Required beam parameters
Stage | KEKB |  | Phase-I |  | SuperKEKB | 
Item | e+ | e- | e+ | e- | e+ | e-
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Bunch charge | Primary e-10nC → 1 nC | 1 nC | Primary e- 4nC → 0.2 nC | 1 nC | Primary e-10nC → 4 nC | 5 nC
Norm.Emittance (ge) (mrad) | 2100 | 100 | 2400 | 150 | 100/20 (Hor./Ver.) | 50/20 (Hor./Ver.)
Energy spread | 0.125% | 0.125% | ±0.5% | ±0.5% | 0.1% | 0.1%
Num. of Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection | 3 rings (KEKB e-/e+, PF) |  | 3 rings (KEKB e-/e+, PF) |  | 4 rings (SuperKEKB e-/e+, PF, PF-AR) | 

## Slide 5: What and when to be improved from KEKB to SuperKEKB
Present in late 2015
  Prepare low-emittance electron & positron to be cooled at DR
Phase-I in early 2016
  Supply for initial ring tuning and beam-duct baking
  Investigate the strategy for emittance-preserved high charge
Phase-II in 2017
  Gradually improve emittance preservation
  Make effort for higher charge
Phase-III in late 2017
  Emittance to be fully minimized with maximum charge

## Slide 6
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV e+
Damping Ring
circ. 136 m
ECS
BCS
RF gun
e+
target
HER
LER
ECS
1.5 GeV
PF
PF-AR
chicane
< e- beam>
Low emittance (  20 mmmrad)
high bunch charge (  5nC)
Photo-cathode RF gun system
Upgrades of Injector LINAC
Positron Damping Ring (DR)
Low emittance e+ beam
Positron Capture Section
- Flux concentrator (FC)
- Large aperture S-band accel. Structures (LAS)
4 times higher e+ yield
Pulsed Quads & Pulsed Steering Magnets
Alignment error tolerance
(local)=0.1mm
(global)=0.3mm
Low emittance preservation
Thermionic gun
(10nC primary e-)
Event Timing System and Pulsed Modules
Synchronization for 5-rings including DR
200 parameters are switched at 50Hz each mode
Optics at the downstream of DR is switched by using pulsed magnets
Thermionic gun @A1
Positron production @14
Collimation @18

## Slide 7: Electrons
Electrons
  for HER
  for making positrons
Development on RF gun for electrons has been much advanced
  Targeting ultimately low-emittance, high-charge beam
  RF gun cavity seems well developed but operation in full spec is required for actual use.
  Considerable work is needed to make stable laser system.
We decided to bring thermionic gun for Phase-I to life
  For positron generation and possibly for electrons in phase-I
  Thermionic gun and RF gun were set in parallel at A1

## Slide 8: Beam Commissioning of RF Gun
Laser: 2bunch, 25 Hz
RF gun acc. voltage: limited to 6.5 MV by breakdown (13.5 MV@design)
Screen monitor (t=30m)
RF GUN
(m)
x=49.2 mmmrad10%
y=26.2 mmmrad10%
Emittance measurement by Quad-scan
Beam size was measured shot by shot.
=> Position jitter is not included
Bunch charge: 3nC@Screen
Measured emittances were higher than target values.
Higher horizontal emittance is due to laser incident angle.
Operation Condition
Target : 5nC
x=50 mmmrad, y=20 mmmrad @ LINAC end
x , y = 10 mmmrad @ Gun
Need high acc. voltage of RF gun for small emittance
(Y,M,D)
1 week
Bunch charge just after RF GUN (A1_C5)
Bunch charge stability depends on the laser stability.
Yb:YAG Thin-disk cooling by soldering Cu plate was Improved.
R. Zhang, TUPWA071
Laser power increased and stability was also improving.
Sort for 3h
Archived 1/10s
4nC/bunch
Miura, Furukawa in B2GM in June 2015

## Slide 9: A1 electron gun area in double-deck configuration
GU-AT
GR-A1
Two lines merge

## Slide 10: Recent electron bunch charge
Out of 6nC, 2 nC was transported through target center hole to linac end
6 nC was delivered to target
In late January, 2016
Radiation shield at target area will be reinforced
Target drive current of 200nA at present will be increased to 800nA with adding iron shield around target area
It allows drive electron with 8nC/bunch in 2 bunched at 50Hz.

## Slide 11: Positron system
For phase-I (without DR)
  Primary drive electron intensity will be increased
  Radiation safety under 800 nA for phase-I will be allowed in late Jan. 2015
  Production rate will be increased with using
  flux concentrator, high solenoid field and large aperture accelerator tube
  Emittance will be reduced by collimation
  Big shield is being prepared for radiation safety

## Slide 12: Schematic of positron Capture Section
KLY
1-5
KLY
1-6
SLED
SLED
LAS 14 MV/m
deceleration & phase slip & acceleration
LAS 10 MV/m
acceleration
Solenoids
target
+FC
LAS : Large Aperture S-band structure
Large Aperture
S-band structure (LAS)
LAS with SLEDs for sufficient field gradient
breakdown issue of LAS in solenoid field
needs careful RF conditioning

## Slide 13: Positron intensity achieved in 1 July, 2015
Kamitani, POSIPOL 2015
Reached h=0.1 before summer shutdown in this year
e+ 0.4nC
e- 4nC

## Slide 14: Boosting positron yield and intensity
Under processing with magnetic field
Done with electricity power up
Under processing with magnetic field
For Phase-I

## Slide 15: Target / FC / LAS / Solenoid
FC & TGT
LAS & Solenoid
Radiation shield
Beam
FC & TGT
FC drive current capacity was doubled in summer 2015
Radiation shield will further increased before phase-I in Jan. 2016

## Slide 16: Struggling against gas burst
Frequent gas burst prevents FC with solenoid field from higher current operation than half-design.
Drive voltage
Gas pressure
Frequent gas burst and vacuum breakdown prevents LAS in solenoid field from higher field operation than 10 MV/m.
RF power
Pressure
ES
24 hours
For both, processing is kept under way.

## Slide 17: Breakdown(?) to be understood and suppress
A few microsec
FC current pulse
Normal
Abnormal
Trailing half was reduced, showing reduction of inductance.
RF Input
RF reflected
RF transmitted
Normal pulse
Abnormal pulse
RF power was reflected back to klystron and interrupting transmission through accelerator tube.
RF power for LAS

## Slide 18: Further development on FC
Replacement of TGT+FC is under consideration for phase-I.
Complete exchange mechanism of the TGT + FC + LAS may be in hand before Phase-II.
TGT+FC
FC chamber

## Slide 19: Positron at present and near future
Positron yield of 10% of drive electron was established.
Higher-charge drive electron makes more positrons.
High voltage cabling and other peripheries are approaching to their final ones.
Frequent gas burst is observed especially with solenoid magnetic field at more than 6kA current for FC.
Processing is a bit slow and we need to understand what is happening to overcome this phenomenon and operate at design current.
LAS (Large-aperture S-band) accelerator tubes are also subject to gas burst and sometimes with RF breakdown. More conditioning time is needed to reach the full accelerator field with SLED.
Exchange mechanism of target and FC was designed.
Exchange mechanism of fully replacing FC system is underway for final phase. This makes possible to replace any of the TGT/FC/LAS/Solenoid hard wares.

## Slide 20: Collimation for phase-I
A set of three collimators were prepared for cutting beam tail for DR injection at the end of sector 1.
These can be used for cutting positron beam tail for Phase-I without DR.
Additional shield is being prepared.

## Slide 21: Emittance issue for phase-II and beyond
Hard wares aligned on a girder by measuring positon by laser tracker
Girder are aligned by using laser PD referred to laser light passage
Hard ware alignment are to be smoothly improved by measuring with laser tracker
Beam evaluation and evaluation to be integrated in the alignment process
Suppression of emittance growth due to the floor movement

## Slide 22: Alignment Requirement
A
B
1
C
2
3
4
5
J-ARC
Rings
500m
120m
Requirement
Local s < 0.1mm
Global s < 0.3mm
  s < 0.1 mm: bge 20 mm·mrad is almost satisfied.
  s > 0.1 mm: emittance preservation is required by some methods.
H. Sugimoto

## Slide 23: Laser PD system as a reference to align girders
Manual ON/OFF
4-segmented silicon PD (dia.=10mm)
500m laser line
Automatic ON/OFF
Linear type
2+8 installed now
Foresee more installation considering pendulum type and/or present type as candidate

## Slide 24: Laser PD measurement Mostly aligned by a year ago, summer in 2014
Ver.
Vertical
Horizontal
PD in automatic measurement system are installed
two in autumn last year and eight in Summer this year
and more to be installed in this fiscal year
PD_28_G6DA
PD_28_REFUA

## Slide 25: Laser PD more near expansion joint
Ver. Same data
as left figure
Vertical
Horizontal
Movement near joint is big.
Mover or some passive support structure to be developed.

## Slide 26: Hard ware initial alignment on a girders in sector 3 - 5
Horizontal
s=34mm
Vertical
s=47mm
Horizontal
Vertical
2015/2/24
26
First round done to install/assign/measure.
From now on, we try to find a series of
alignment chances to improve smoothness.
the stability of this alignment should be confirmed.

## Slide 27
Floor configuration
DR
ECS
BCS
Gun
HER
LER
ECS
PF
PF-AR
e+ target
Expansion joint
C 1 2 3 4 5
B A
Laser PD continuous measurement devices
Half a year data in next page

## Slide 28: Movement in half a year
 Upstream PD_28_G6DA
PD_28_REFUA Downstream 
4.25 m
Movement of 1mm order was observed in half a year.
Daily movement is of the order of +/- 0.15mm.
Positive correlation was observed.
Correlation between these two positions.

## Slide 29: Status and near future strategy
Monthly measurement of relevant PD’s are kept in best effort base for more than a year.
Continuous PD measurement at 10 points are in progress and acquire data over a year.
More automatic PD’s will be made and installed.
Movement at joint is underway to understand movement.
Beam study will be performed to acquire the feasibility of floor movement information by beam.
Feasibility of mover will be studied in mechanism, time, cost.
These efforts should be integrated to make a system before Phase-III, in two years from now.

## Slide 30: Conclusion
Phase-I beam, both electrons and positrons, can be delivered in time in 2016.
  Thermionic gun, positron production, shield reinforcement, ….
Preparation for DR will be made by next summer and supply “low” emittance beam will be delivered in Phase-II from 2017.
  RF-gun, LTR/RTL, pulse magnet, …..
Floor movement should be understood and we develop a suppression / compensation scheme to meet Phase-III operation in 2018.
  Floor movement and emittance control, ultimate laser RF-gun, …

## Slide 31
SuperKEKB
dual rings
Mt. Tsukuba
Injector Linac
PF-AR
PF
Thank you