## Slide 1
KEK / Fujio Naito
How J-PARC recovered from
the big earthquake
Outline
About J-PARC
The earthquake
Damage on J-PARC
Recovery plan
Beam study results
Summary

## Slide 2
2
Nuclear Transmutation
(Phase 2)
Joint Project between KEK and JAEA
Materials and Life Science
Experimental Facility (MLF)
Hadron Beam Facility
５００ｍ
Linac
181MeV(400MeV)
Neutrino to Kamiokande (T2K)
3-GeV Rapid Cycle Synchrotron (RCS)
(25 Hz, 270kW (1MW) )
30(50)-GeV Main Synchrotron Ring (MR)
( 200kW (0.75 MW) )
J-PARC
(Japan Proton Accelerator Research Complex)
Pacific Ocean

## Slide 3
Main Synchrotron Ring (MR)
(30 (50) GeV, Period: 2.6~6.0sec, φ500ｍ）:
ν-beam line（Super Conducting Mag.）
Rapid Cycle Synchrotron (RCS)
（3GeV, 25Hz, φ100ｍ）
Linac（E:181MeV-> 400MeV (2013)
L:120m -> 25０m ）

## Slide 4
→ Design beam power : 1MW for MLF & 750kW for T2K
(current beam power is 0.2 MW for both experiments)
Nuclear & Particle Physics at 30 GeV
Materials & Life Sciences at 3 GeV
Proton (p)
3 GeV, 30 GeV
Goals at J-PARC

## Slide 5
Disaster we had in March 2011
The biggest earthquake (Mar., 11, 14:46)
Tsunami near J-PARC (Mar., 11, 16:52)
First hydrogen explosion of the nuclear power plant in Fukushima (Mar., 12, 15:36)
Beam was provided to all users from April 2009.
Users run of JFY2010 was stopped as scheduled at 7:00 on March 11, 2011.
Just linac group continued the beam study in the daytime…..

## Slide 6
March 11, 2011
1st 01:54
2nd 06:45
3rd 07:44
4th 14:46
.
.
78th 23:56
The Great East Japan Earthquake
Seismic intensity map of the main shock on March 11, 2011, and epicenter distribution from March 11 to 18, 2011.
by National Research Institute for Earth Science and Disaster Prevention (NIED)

## Slide 7
Tsunami
simulation result
near J-PARC
J-PARC
Tsunami max height : 6.6 m
Tsunami Protection : 8m
Tokai nuclear power plant
Tsunami max height : 5.4 m
Tsunami Protection : 6.1m
(On Mar. 09 2011, 3.3m -> 6.1m)

## Slide 8
J-PARC
Broken
reactors
Riken
Air dose rate measured by an airplane
(April 2011)

## Slide 9
On March 17 the water level was only 1 cm, but it increased to 10 cm (100 tons) on March 24. The water was pumped out with a rented electric generator. PH=11 and tons of acid were necessary to neutralize water.
Linac Tunnel on March 24, 2011

## Slide 10: Linac measured position (Apr. 2011)
Beam axis[mm]
Horizontal direction [mm]
Vertical direction [mm]
Longitudinal direction[mm]
~0.03mrad
Red broken line：New beam line after the earth-quake

## Slide 11
4177 左の影が大きい
Rapid Cycle Synchrotron (RCS, 3GeV)
No serious damages on the equipment/instruments in RCS tunel.
Position of all equipment/instruments were measured.
The maximum displacement is 3.7mm vertically & 10mm horizontally.
Blue : Reference positions of the magnet
Red: Measured positions after the earthquake
(Please note the magnitude of displacement is amplified x2000.)

## Slide 12
4177 左の影が大きい
Magnet displacement from
the reference line
Green : vertical direction
Red : horizontal direction
Blue : beam deirection
Main Synchrotron Ring (MR, 30GeV)
・ There were no serious damages on all MR equipment/instruments, such as magnets.
It, however, appeared they misaligned in both vertical and horizontal directions.
・ Some magnets misaligned greatly are re-aligned with replacing a stage.
・ Inspection of the RF power amplifying system has been completed.
Orange : Reference positions of the magnet
Blue & Red: Measured positions after the earthquake (Please note the magnitude of displacement is amplified x2000.)
Amplified x2000

## Slide 13
Demand
from users (MLF, T2K) and the law fixed the MLF budget:
Results:
*Linac must be re-aligned but V-shape is approved.
*RCS is usable without re-alignment if power ≤ 300kW
*MR must be re-aligned.
Beam simulation
to keep the beam loss as same as before:
Beam must be supplied to users during JFY2011 at least approximately two months.
>> Minimum repair of the broken building has been done to resume the beam acceleration as soon as possible.
Notes: J-PARC has the fund supported by the special law in Japan that promotes the usage of beam for users of big accelerators. It requires the results that users have gotten the beam in any fiscal year. If there is no such result, the fund is cut off.

## Slide 15
History of beam delivery from RCS to MLF
In the last three days, 275 kW beam was delivered to MLF.
Stable operation of 275 kW was successfully demonstarted.

## Slide 16
History of beam delivery from MR to the T2K experiment
Operation for beam delivery to the T2K before summer 2012 was finished on June 9.
T2K accumulated the beam of ~3x1020 POT.

## Slide 17
Summary
Although J-PARC had the big damage by the earthquake, it has been fixed in minimum to accelerate the beam.
J-PARC resumed to accelerate beam from Dec., 2011.
Experiments by user restarted in Jan., 2012.
However a lot of troubles of the earthquake origin(?) still happen in the accelerators.
Damage on the accelerator buildings of linac (wall, doors, cranes, floor) and MR (expansion joints, ground-water leakage) is not fixed yet.
RCS will realign the all magnets in the summer of 2013.

## Slide 18
Thank you very much!

## Slide 19
Leaking water depth in the LINAC tunnel reached to 10 cm.
After recovery
LINAC
The approach to the LINAC entrance subsided more than 1 m. In contrast, the front road raised a few 10s cm.
Still under the construction
The road around the 3 GeV subsided more than 1 m at many places.
3 GeV Synchrotron
Re-leveled the basis
The basis for transformers subsided ~1 m.
After recovery
Recovery Status of J-PARC from Damages by the 3.11 Earthquake
Damages and Recovery Status of Accelerator Facilities
Fortunately no victims at J-PARC, but severe damages on the facilities, such as piping systems, power devices, and instruments. We also had land subsidence at many places around buildings, water leaks, and misalignment of electromagnets and shielding blocks.
added concrete basis

## Slide 20
NaI -survey meter
GM-survey meter
Dose rate in KEK Tsukuba campus

## Slide 21: Linac major parameters
  Accelerated particles: H- (negative hydrogen)
  Energy: 181 MeV, The last two SDTLs are debunchers
  (400 MeV for ACS, 600 MeV for SCL)
  Peak current: 30 mA (50 mA for 1MW at 3GeV)
  Repetition: 25 Hz (additional 25 Hz for ADS application)
  Pulse width: 0.5 ms (Beam), 0.6 ms (RF)

## Slide 22
Observation of the shadow of
the DT by an alignment telescope
Displacement ?
Normal
Inside view of the DTL
before installation
Drift Tubes in DTL

## Slide 23: Alignment result of the linac
Horizontal
Vertical
Position
Z
DTL
SDTL
MEBT2
A0BT
L3BT
Bending angle at DTL end : 0.91-mrad horizontaly, 0.28-mrad vertically.
In the SDTL & A0BT section, the displacement is 1.5-mm in maximum for horizontal direction.

## Slide 24
Beam loss in RCS with the beam > 400 kW
P-BLM signals
Before the earthquake
P-BLM signal (V)
P-BLM signal (V)
300 kW
420 kW
Collimator
Arc
Extr.
Arc
RF
Arc
Inj.
No large difference
in beam loss
After the earthquake
Beam loss increased after the earthquake for 420 kW
Particle loss before the earthquake：~ 0.4%
Particle loss after the earthquake： ~ 0.8%
Significant difference
in beam loss
In the summer of 2013, the entire
adjustment of the RCS will be done
BLM ID#

## Slide 25
Linac:
* HV terminals of Ion pump have the discharge problem.
* Almost temperature sensors were corroded.
* A HV rectifier in the oil tank for the Klystron was broken.
* Humidity in the tunnel is still high by the leakage of ground water.
* Cranes are still not usable.
* Floor is broken and tilted.
RCS:
MR:
* New leakage of the ground water found in the tunnel.
*Twisted expansion joints of the tunnel are not fixed.
Exp:
* Power supply of the magnetic horn for T2K was broken.
Problems after the beam resumption

## Slide 26
Neutrino Oscillation (T2K) Experiment
ν
e
ν
τ
ν
μ
T2K
Atmospheric Neutrino
Accelerator Neutrino
Solar Neutrino
Reactor Neutrino
KamLAND, SNO
Kamioka,
K2K,
MINOS,
etc.
Goal is to measure sin22θ13 down to 0.01
Electron neutrinos
Mu neutrinos
θ13 Mixing between the 1st and 3rd generation
Competition with Double Chooz, Daya Bay, FNAL, etc.

## Slide 27: T2K electron neutrino candidates