## Slide 1: CERN’s Proton Synchrotron complex operation teams and diagnostics applications
Marc Delrieux, CERN, BE/OP/PS
  CERN’s Proton Synchrotron (PS) complex
  How are we involved?
  Review of some diagnostics applications
    examples of 3 possible scenarios for operations
Workshop on Accelerator Operations
SLAC National Accelerator Laboratory
Diagnostics 07/08/2012

## Slide 2: CERN’s Protron Synchrotron complex (1/4)

## Slide 3: CERN’s PS complex (2/4)
Linac 2, 1978-?
  Protons source
  Radio-frequency quadrupole
  2 buncher cavities (and 1 debuncher)
  3 Alvarez drift tubes tanks
  Bringing protons to a kinetic energy of 50 MeV, with a beam current up to 180 mA, each 1.2 s

## Slide 4: CERN’s PS complex (3/4)
PS booster, 1972-?
  4 superimposed synchrotrons of 157 m circumference, injecting a certain quantity of Linac 2’s pulses via a multi-turns injection process
  Captures 0, 1 or 2 bunches per ring, hence providing up to 8 bunches to the PS each 1.2 s, with a kinetic energy of 1.4 GeV
  Wide intensity spread: 5E09-4E13 protons per cycle
  A dedicated experimental area (ISOLDE), which consumes almost 40% of produced cycles (and a huge quantity of protons!)
  Space charge effects, tune shift
  Critical for intensity and transverse beam
  characteristics (hence LHC luminosity)

## Slide 5: CERN’s PS complex (4/4)
Proton Synchrotron, 1959-?
  Has accelerated/decelerated
    Protons/antiprotons
    Ions
    Electrons/positrons
  Combined-function magnets
  Very versatile Radio-Frequency system
    accelerating cavities (3.3-10 MHz)
    “gymnastics” cavities (20, 40, 80, 200 MHz).
  Wide harmonics range (h7 to h420), numerous manipulations
    bunch splitting, bunch merging, batch compression, batch expansion, bunch rotation…
  Various extraction energies (up to 26 GeV)
  All operational beams cross transition (Transition energy 6.1 GeV).
  Fast, slow, and multi-turn extractions (5 turns continuous transfer…)
  Critical for longitudinal beams characteristics.
  Dedicated experimental areas (East Hall, nTOF), and other client machine (Antiproton Decelerator)
The ions LHC injectors chain also involves Linac3 and LEIR (Low Energy Ion Ring) but these are not operated by PS teams

## Slide 6: How are we involved in applications?
Since 1959, some of our applications have slightly evolved…
Groups developing applications
  Controls
  Beam instrumentation
  Operation
Each shift leader is linkman for a certain topic
  Analogue signals observation
  Beam intensity measurements
  Longitudinal profile measurements
  Beam losses measurements
  Orbit measurements and corrections
  Transverse profile measurements
  Working point
  Magnetic cycles
  …and also: Controls system, power converters and magnets, beam documentation, Frequency domain measurements, Timing and sequencing, safety…
A linkman’s tasks: write specifications, test applications, report issues, follow-up, train fellow operators, ensure the applications fulfill expectations
A tool for follow-up: from our e-logbook, “report OP issues”

## Slide 7: 1st (most frequent) scenario: let them do the job
PS orbit (Beam Instrumentation)
  40 pick-ups, up to 200 000 measurements
  Trajectories (turn-by-turn, bunch-by-bunch),
  orbits, mean radial position, phase space reconstruction
  OP input permanently necessary
    Succession of harmonics for gates
  Very good reaction and follow-up
Analog signals
  >1800 signals
  OP functionalities
    Memory, survey…
    Multi-triggering and analysis
  Piquet service

## Slide 8: 1st (most frequent) scenario: let them do the job
Controls system
  Knobs and working sets
  Analog functions editor
OP requirements
  Piquet service
Equipment groups
  PS main power supply
  Specialists application and interface
  but adapted following OP requirements

## Slide 9: 1st (most frequent) scenario: let them do the job
Fixed displays
  OP requirements to help fast diagnostics
    Intensities, magnetic cycles, destinations, particles types…
Alarms
  Adapt an already existing program to PS complex
  Integrate commands
  Integrate frontends monitoring

## Slide 10
In general CERN-(too)-generic applications
  LHC is so different from our small pulsed accelerators!
  Development for LHC is the priority
  So many different beams = so many different settings
  Exotic processes and manipulations
Wire scanners, tune and chromaticity measurements…
2nd scenario: adapt application
to your needs

## Slide 11
Specific, dedicated applications
  RF gymnastics
    Bunch shape measurements
  Working point control
    Combined-functions magnets
    + additional windings
    + low-energy quadrupoles
  Pulsed accelerators
    Samplers
Requires heavy maintenance
  In any case, you have to use controls tools and follow their standards
3rd scenario: do it yourself

## Slide 12
If you have a dedicated controls/applications group
  Try to get involved as early as possible
  Write specifications
  Find compromises
  Make sure developers do what YOU want
  Ask a piquet service for applications YOU consider critical
  Make sure you have efficient issues reporting tools
If some operators are able to code (and no one gets offended)
  Either adapt existing applications to your needs
  Or do 100% of the work…but OP can’t provide the same infrastructure as a dedicated group
Thank you for your attention, and…how do you get what you want?
Conclusions