## Slide 1: KEK/Japan – CERN Collaboration on Linear Collider Studies
Collaboration on LC detector and physics study
Collaboration on CLIC/ILC machine study
  Status of CDR
  Highlights of ongoing collaboration
Plans at CERN in the coming years

## Slide 2: ILD detector concept studies Physics, event generation + grid LCFI flavour tagging for LC
Active, though informal, collaboration between KEK and CERN on Linear Collider Detectors. For ILC and CLIC, based on ILD detector concept.
Collaboration based on mutual interest.
Particular mention of collaboration:
Various editors of the CLIC physics&detector CDR editing:
A. Miyamoto (KEK), Y. Makida (KEK), T. Matsuda (KEK), T. Takeshita (Shinsu Univ.)
Collaboration on physics studies, event generation, and grid production at KEK and CERN:
A. Miyamoto (KEK), T. Tanabe (Univ. of Tokyo)
Common LCFI flavour tagging package for Linear Collider:
By Univ. of Tokyo (T. Tanabe, T. Suehara), KEK, etc.
R&D on Linear Collider TPC with GEMs and Pad readout
SAltro16 electronics: K. Fujii (KEK), T. Matsuda (KEK) et al.

## Slide 3: Detector magnet system R&D
Collaboration with KEK on:
  Common R&D on reinforced superconductor for ILC and CLIC detector solenoid.
  Expert contribution from KEK highly appreciated (A. Yamamoto, Y. Makida)
  Development of materials for conductor reinforcement
  Extrusion test of a large reinforced conductor KEK ATLAS-type (done in 2011) => tests are ongoing.
ILD detector solenoid
4 Tesla, 3.4 m inner bore

## Slide 4: Accelerator Collaboration with KEK
Key topics:
  X-band structure development and testing (T. Higo et al.)
  ATF2-3 activities (N. Terunuma, J. Urakawa, T. Tauchi, …)
Collaborations within the CLIC- ILC working group framework
  General Issues (K. Yokoya et al.)
  Sources (T. Omori et al.)
  Damping ring beam dynamics (K. Kubo et al.)
  Beam dynamics from damping ring to IP (K. Kubo et al.)
Generic (often informal) collaborations on many fundamental topics
  Recent CAIN vs. GUINEA-PIG benchmarking (K. Yokoya)
  Electron cloud (K. Ohmi et al.)
  Two-stream instabilities (K. Ohmi, K. Oide et al.)
  Coherent synchrotron radiation (K. Oide et al.)
    Super-KEKB and CLIC damping ring have similar (potential) problem
  BDS + Collision Point (T. Tauchi)

## Slide 5: CLIC Accelerator CDR Status
Accelerating structure
Drive beam generation
PETS
Two beam module
Drive beam deceleration
Main beam emittance generation and preservation, focusing
Alignment and stabilisation
Experimental conditions
Machine protection/operation
Had defined feasibility issues
All have been addressed
Great progress
Certainly more work for the future
Will turn into performance issues
CDR is progressing
drafts of all chapters
most are submitted as final and with editors
Very grateful for help of N. Toge in editing the report

## Slide 6
150 MeV e-linac
Combiner ring
Experimental area
28 A - 140 ns
Delay Loop
CLIC Test Facility (CTF3)
3.5 A – 1200 ns
Thermionic source
Photo injector
TBTS (two-beam test stand)
power transfer to main beam
module design
TBL (test beam line)
drive beam stability during deceleration

## Slide 7: TBTS and TBL Results
Consistency between
produced power
drive beam current
test beam acceleration
Maximum gradient 145 MV/m
Total power produced ~500MW
Deceleration 27MV
(of 117MeV beam)

## Slide 8
Fabrication – 6/7 of the above tests, with all best results achieved with KEK-coordinated machining of structures.
Testing – 4/7 with best performance of all categories of structures in tests made in NEXTEF at KEK.
High-gradient science – Extensive measurements of high-gradient rf instrumental in developing theory.
KEK’s Fundamental Contributions to 100 MV/m Accelerating Structures
International Workshop on
Breakdown Science and High Gradient Technology
April 18-20, 2012 at KEK

## Slide 9: ATF 2
We are impressed how quickly ATF2 is recovering
We had proposed a number of topics for future collaboration
Currently our main focus is on
Small beam size (optics design / tuning)
Ground motion and feedback/feedforward studies
  Equip magnets with ground motions sensors and correlate magnet and beam motion
  Detailed study of expected correlation by Yves Regnier
  LAPP already bought sensors
  Will need 6 Hz operation and little beam jitter
New extraction kicker for ATF
  Kicker design being finalised, prototype in 2012
  Adaptive adder
    Small scale protype next year
    Full system ready in mid to end of 2013, second system maybe in summer 2014

## Slide 10: QF1 and QD0 Magnets for ATF2/ATF3
 | QF1 | QD0
Aperture radius | 40 mm | 35 mm
Magnet length | 512 mm | 475 mm
Yoke height ×width × length | 290 mm × 290 mm × 455 mm | 280 mm × 280 mm × 455 mm
Effective length | 474 mm | 473.1 mm
Nom. field gradient at Z=0 mm | 6.9 T/m | 12.5 T/m
Nom. Integrated field gradient | 3.27 T | 19.2 T
Tuning range | 9.2% | 7%
Gradient tuned by | Coils | Movable blocks
Coil parameters |  | 
Number of turns per pole | 35 | 
Conductor size | 4 mm × 4 mm | 
Current | ± 20 A | 
Max. current density | 1.2 A/mm2 | 
Cooling | Air, natural convention | 
Study (E. Marin) shows
would profit from re-ordering quadrupoles
a better final doublet
M. Modena designed new magnets
can be built on request
delivery spring/summer 2013

## Slide 11: Objectives and Plans for 2012-16
Develop the technical design basis. i.e. move toward a technical design for crucial items of the machine and detectors, the MD interface, and the site.
Priorities are the modulators/klystrons, module/structure development including testing facilities, and site studies.
Technical work-packages providing input and interacting with all points above
Identify and carry out system tests and programs to address the key performance and operation goals and mitigate risks associated to the project implementation.
The priorities are the measurements in: CTF3+, ATF and related to the CLIC Zero Injector addressing the issues of drive-beam stability, RF power generation and two beam acceleration, as well as the beam delivery system.
Technical work-packages and studies addressing system performance parameters
Notes: Add some info about space at CERN

## Slide 12
World-wide CLIC&CTF3 Collaboration
Gazi Universities (Turkey)
Helsinki Institute of Physics (Finland)
IAP (Russia)
IAP NASU (Ukraine)
IHEP (China)
INFN / LNF (Italy)
Instituto de Fisica Corpuscular (Spain)
IRFU / Saclay (France)
Jefferson Lab (USA)
John Adams Institute/Oxford (UK)
Joint Institute for Power and Nuclear Research SOSNY /Minsk (Belarus)
PSI (Switzerland)
RAL (UK)
RRCAT / Indore (India)
SLAC (USA)
Sincrotrone Trieste/ELETTRA (Italy)
Thrace University (Greece)
Tsinghua University (China)
University of Oslo (Norway)
Uppsala University (Sweden)
UCSC SCIPP (USA)
ACAS (Australia)
Aarhus University (Denmark)
Ankara University (Turkey)
Argonne National Laboratory (USA)
Athens University (Greece)
BINP (Russia)
CERN
CIEMAT (Spain)
Cockcroft Institute (UK)
ETH Zurich (Switzerland)
FNAL (USA)
John Adams Institute/RHUL (UK)
JINR (Russia)
Karlsruhe University (Germany)
KEK (Japan)
LAL / Orsay (France)
LAPP / ESIA (France)
NIKHEF/Amsterdam (Netherland)
NCP (Pakistan)
North-West. Univ. Illinois (USA)
Patras University (Greece)
Polytech. Univ. of Catalonia (Spain)
CLIC multi-lateral collaboration - 43 Institutes from 22 countries
Several others in the process of being added or being linked to the CLIC efforts through common technical developments

## Slide 13: Work-Packages and Responsibilities
The programme combines the resources of collaborators inside the current collaboration, plus several new ones – and also involves around 20 CERN groups:
Have ~75 submitted descriptions of ongoing or planned efforts linked to these work-packages 2012-16 from groups outside CERN (result of CLIC working meeting 3-4.11: https://indico.cern.ch/conferenceOtherViews.py?view=standard&confId=156004 (still open for more interests)
5 from KEK
Description of contributions, link-persons, planned personnel and material resources at home and at CERN for the period

## Slide 14: Conclusion
Have strong collaboration between KEK and CERN on different R&D topics
  Profits for CERN
    X-band accelerating structure tests and expertise
    ATF/ATF2
    Detectors
    Positron source studies
    Intellectual exchange
    …
  Can hopefully also bring some profits for KEK
Should continue and deepen the effort