## Slide 1: Study of high gradient acceleration
High gradient long-term evaluation of prototypes
X-band GLC in early 2000
Collaboration since 200 7 to date
Main acc. in two-beam scheme
1 TeV e+e-
3 TeV e+e-
Magnetic field plays a key role
Next 5 years
Crystal movement during a pulse
Hard copper is better?
High energy
Fundamental studies focusing on crystal characteristics
Serve for stable operation of normal conducting linacs in various aspects
Study and develop LC prototype structures in collaboration
Heavily damped cell
Simple geometry & well-defined copper
Breakdown is one of the key measures of feasibility
Notes: 生出さんへ
常伝導高電界加速の開発研究の意義
2000年代前半まで X-band GLC として展開
2007年以降 共同研究の一環として継続 CLICの主加速器の高電界加速の研究
各々、数ヶ月にわたるプロトタイプ加速管の試験を通じてわかってきた
１．真空放電の抑制が問題
２．表面磁場の影響が大きいらしい（特に強減衰加速管の磁場増大部）
表面温度上昇→表面劣化→金属疲労 等も関連している
３．表面電流強度の大きい場所 1A/μm＾2 級
電界が殆ど無いはずの場所にも放電様の痕跡が見え、「Electromigration」の現象とも考えられる
今後、高電界を必要とする加速器に対する研究として
上記の磁場関連以外、ゴミや汚れの抑制技術等の開発が必要である。
しかもその基盤技術の理解が必須であること重要と考える。
アクションプラン
１．放電メカニズムを理解するための基礎研究
２．現有、新規加速器の高電界加速部へ知見、技術の展開
３．LCプロトタイプ試験を通じた加速管の開発
これを通じて、
小型の加速器への応用を含めて、高電界での安定運転への貢献を目指す。