## Slide 1
Overview of the CLIC study

## Slide 2
500 GeV c.m.
3TeV c.m.
1.5 TeV c.m.
What is CLIC?
A highly developed concept, design and hardware study for a collider capable of delivering e+e- physics in the energy decade of 0.3 to 3 TeV – the lepton physics compliment to the LHC.

## Slide 3
Current CLIC Collaboration
Gazi Universities (Turkey)
Helsinki Institute of Physics (Finland)
IAP (Russia)
IAP NASU (Ukraine)
IHEP (China)
INFN / LNF (Italy)
Instituto de Fisica Corpuscular (Spain)
IRFU / Saclay (France)
Jefferson Lab (USA)
John Adams Institute/Oxford (UK)
Joint Institute for Power and Nuclear Research SOSNY /Minsk (Belarus)
PSI (Switzerland)
RAL (UK)
RRCAT / Indore (India)
SLAC (USA)
Sincrotrone Trieste/ELETTRA (Italy)
Thrace University (Greece)
Tsinghua University (China)
University of Oslo (Norway)
University of Vigo (Spain)
Uppsala University (Sweden)
UCSC SCIPP (USA)
ACAS (Australia)
Aarhus University (Denmark)
Ankara University (Turkey)
Argonne National Laboratory (USA)
Athens University (Greece)
BINP (Russia)
CERN
CIEMAT (Spain)
Cockcroft Institute (UK)
ETH Zurich (Switzerland)
FNAL (USA)
John Adams Institute/RHUL (UK)
JINR
Karlsruhe University (Germany)
KEK (Japan)
LAL / Orsay (France)
LAPP / ESIA (France)
NIKHEF/Amsterdam (Netherland)
NCP (Pakistan)
North-West. Univ. Illinois (USA)
Patras University (Greece)
Polytech. Univ. of Catalonia (Spain)
CLIC multi-lateral collaboration - 48 Institutes from 25 countries
Over the last months increased to 48 institutes from 25 countries adding Jerusalem, Belgrade, Alba and Tartu to the list – linked to 2012-2016 work-programme
On-going discussions with 5 more groups …

## Slide 4: Organisation of CLIC detector and physics study
Pre-collaboration structure, based on a “Memorandum on Cooperation”
http://lcd.web.cern.ch/LCD/Home/MoC.html
Light-weight collaborative structure => partners join on “best effort” basis
Organisation resembling most particle physics experiments
Central body is the Institute Board

## Slide 5
Primary accelerator features
Reach the high end of the energy range through high, 100 MV/m, accelerating gradient by using short-pulse, around 200 ns, normal-conducting rf.
Deal with the resulting high peak power requirement by going to high rf frequency, X-band, produced by the so-called drive beam scheme. At the lowest energies it is also possible to use klystron/rf pulse compressor units. Accelerating structure input powers are around 250 MW/m.
Deal with the luminosity and resulting high average power requirement by producing, transporting and colliding low-emittance, multi-bunch beams. This requires high-performance damping rings, micron-level main-linac precision and alignment, accelerating structure higher-order-mode damping, nanometer-level main-linac quadrupole stabilization and a sub-nm stabilized final focus etc.

## Slide 6: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 7: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex
140 ms train length - 24  24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
24 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - initial
Drive beam time structure - final

## Slide 8: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 9: Possible CLIC stages studied
Key features:
High gradient (energy/length)
Small beams (luminosity)
Repetition rates and bunch spacing (experimental conditions)

## Slide 10
The physics and accelerator studies of CLIC have been documented in a CDR which was released last year:
Vol 1: The CLIC accelerator and site facilities (H.Schmickler)
- CLIC concept with exploration over multi-TeV energy range up to 3 TeV
- Feasibility study of CLIC parameters optimized at 3 TeV (most demanding)
- Consider also 500 GeV, and intermediate energy range
- Complete, presented in SPC in March 2012 https://edms.cern.ch/document/1234244/
Vol 2: Physics and detectors at CLIC (L.Linssen)
- Physics at a multi-TeV CLIC machine can be measured with high precision, despite challenging background conditions
- External review procedure in October 2011
- Completed and printed, presented in SPC in December 2011 http://arxiv.org/pdf/1202.5940v1
Vol 3: “CLIC study summary” (S.Stapnes)
- Summary and available for the European Strategy process, including possible implementation stages for a CLIC machine as well as costing and cost-drives
- Proposing objectives and work plan of post CDR phase (2012-16)
- Completed and printed, submitted for the European Strategy Open Meeting
in September http://arxiv.org/pdf/1209.2543v1
In addition a shorter overview document was submitted as input to the European Strategy update, available at:
http://arxiv.org/pdf/1208.1402v1

## Slide 12
Outline
I will now cover R&D on some of the most critical performance issues of the accelerator.
High-gradient acceleration
Peak power production
Low emittance generation and preservation
A little bit of the detector
Project planning
And using our technology for other applications

## Slide 13
100 MV/m gradient X-band accelerating structures

## Slide 14
CLIC accelerating structure development
In order to reach 3 TeV with a facility which, for example, could be built in the area around CERN, so < 40 km, an accelerating gradient of around 100 MV/m is required.
In order to maintain low beam emittance along the main linac, accelerating structures must be built with a few micron tolerances and aligned along 10s of meters with roughly 10 micron tolerances.
In addition, in order to provide sufficient luminosity in an energy efficient way, trains of bunches are accelerated. This means that accelerating structures must be equipped with higher order mode in order to suppress long-range wakefields.

## Slide 15
How we got there: High-power design laws
The functions which, along with surface electric and magnetic field (pulsed surface heating), give the high-gradient performance of the structures are:
global power flow
local complex power flow
New local field quantity describing the high gradient limit of accelerating structures.
A. Grudiev, S. Calatroni, W. Wuensch (CERN). 2009. 9 pp.
Published in Phys.Rev.ST Accel.Beams 12 (2009) 102001
Hs/Ea
Es/Ea
Sc/Ea2

## Slide 16: Simplified Parameter Diagram
Drive Beam Generation Complex
Pklystron, Nklystron, LDBA, …
Main Beam Generation Complex
Pklystron, …
Two-Beam Acceleration Complex
Lmodule, Δstructure, …
Idrive
Edrive
τRF
Nsector
Ncombine
fr
N
nb
ncycle
E0
fr
Parameter Routine
Luminosity, …
Ecms, G, Lstructure
Variable | Meaning | Current value
Idrive | Drive beam current | 101A
Edrive | Drive beam energy | 2.37GeV
τRF | Main linac RF pulse length | 244ns
Nsector | Number of drive beam sectors per linac | 4
Ncombine | Combination number | 24
fr | Repetition rate | 50Hz
N | Main beam bunch charge in linac | 3.72e9
nb | MB bunches per pulse | 312
ncycle | Spacing between MB bunches | 6 cycles
E0 | MB energy at linac entrance | 9GeV
Ecms | Centre-of-mass energy | 500GeV
G | Main linac gradient | 100MV/m

## Slide 17: Optimization Ingredients
Define a figure of merit (FoM) to evaluate one given CLIC design/parameter set
  e.g. FoM=-cost
Define a few free parameters to fully describe the design/parameter set
  The other parameters are unambiguously defined by the free parameters
  Currently: gradient G and a few structure parameters (fRF, Δφ, a, Δa, LS, …)
Use optimisation algorithm to find maximum
FoM(free parameters)
  Currently: a simple full search
Allow some human intervention

## Slide 18
TD18#3 at SLAC
TD18#2 at KEK
Stacking disks
Temperature treatment for high-gradient developed by NLC/JLC
How we got there: heat treatment and material structure
Attempting to understand why it works.

## Slide 19
Micron precision turning and milling
Accelerating structure tolerances drive transverse wakefields and off-axis rf induced kicks which in turn leads to emittance growth – micron tolerances required.
Multi-bunch trains require higher-order-mode wakefield suppression – cells require milled features.
High-speed diamond machining also seems to be beneficial for high-gradient performance through minimizing induced surface stresses.
Development done “in industry”

## Slide 20
Evolution of machining capability
Up to the 1980’s
1980’s - 1990’s
2000’s - 2010’s
Larger machines
Multiple axis ( X/Y/Z and C)
Future ?
Intelligent machines ?
  Robotisation ?
Pallet machining?
  Robotisation ?
First machines at research institutes and universities
Start of industrialization
Optical recording
contact lenses
Single point diamond turning
Up to the 1990’s
1990’s - 2000’s
2010’s
Future ?
Ultra precision diamond milling (lagging more than a decade behind on turning)
Limited to fly cutting
mirror optics
Laser scanner mirrors
First proto type machines
Micro fluidics
Accelerator parts
Milling as add-on on lathes
Lens arrays
Intra ocular lenses

## Slide 21
Klystron-based test stands for CLIC
NEXTEF at KEK
XBox1 at CERN
ASTA at SLAC?
Xbox-2 at CERN based on XL-5
Xbox-3 at CERN based on 6 MW tube

## Slide 22
Accelerating gradients achieved in tests.
Status: 4-9-2012
HOM damped
KEK production/test

## Slide 23: Site preparation
21.02.2013
08.05.2013
Pre-approved by safety for radiation and seismic risks (more to come)
Shielding reinforced, area cleared,
Utilities to be deployed during summer
Modulator in place. Walls to be closed now.
Continuous work

## Slide 24: Two-Beam Acceleration
TD24
Maximum stable probe beam acceleration measured: 31 MeV
 Corresponding to a gradient of 145 MV/m
Two-Beam Acceleration demonstration in TBTS
Up to 145 MV/m measured gradient
Good agreement with expectations (power vs. gradient)
CLIC Nominal, loaded
CLIC Nominal, unloaded
Drive beam ON
Drive beam OFF

## Slide 25
Power production: Two-beam scheme

## Slide 26
Drive-beam power production
The basic idea:
To feed all the energy the collider needs into a long 140 μs, 4.2 A, 2.4 GeV bunched train using 1 GHz rf klystrons and fully loaded low gradient accelerating structures. Very efficient!
Do ‘beam pulse compression’ using a delay loop and combiner rings to take the current up to 100 A. Counter feed these pulses from the accelerator center, which is another step of pulse compression.
Decelerate the beam in 25 cm long low-impedance rf structures called PETS (Power Extraction and Transfer Structures) to produce output powers of 120 MW to feed two accelerating structures.
To test all this, as close as we can to full specifications, we have a test facility called CTF3.

## Slide 27: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 28: CLIC Test Facility (CTF3)
High current, full
beam-loading operation
Operation of isochronous lines and rings
Bunch phase coding
Beam recombination and current multiplication by RF deflectors
12 GHz power generation by drive beam deceleration
High-gradient two-beam acceleration
4 A, 1.4us
120 MeV
30 A, 140 ns
120 MeV
30 A, 140 ns
60 MeV

## Slide 29: Drive Beam Generation
SiC load
damping
slot
10 m
RF pulse at output
RF pulse at structure input
95.3% RF to beam efficiency
Stable high current acceleration
Current stability
Isochronicity, phase coding
Factor 8 current & frequency multiplication
Pulse charge measurement
Full beam loading acceleration
Factor 8 combination
Most RF power
to beam
High beam current
RF in
No RF to load
“short” structure – low Ohmic losses

## Slide 30
L-band klystron development
CLIC drive beam klystron not so different from ILC klystron but at 1 GHz (ILC 1.3 GHz) and with a target efficiency of 70% (ILC 65%), 140 μs (ILC 1.5 ms) and a higher peak power around 15-20 MW (ILC 10 MW).
Detailed scaling studies now beginning to understand potential performance based on existing technology.
ILC 1.3 GHz multi-beam klystrons

## Slide 31
Surface electric field
Surface magnetic field
PETS – fundamental mode characteristics
Beam-driven structure so power rises quadratically with current and length,
135 MW for 100 A beam
213 mm active length
Maximum fields at output with values,
Esurf=56 MV/m
ΔT=1.8 (Hsurf=0.08 MA/m)
Sc=1.2 MW/mm2

## Slide 32
load
Reflection
Transmission
ASTA test PETS version with damping slots and damping material (SiC)
Low RF power measurements
June 2010

## Slide 33: Power Production & Drive Beam Deceleration
33
TBTS:
Power production in PETS (Pout≈ 200MW)
Breakdown rates checked
On-off mechanism tested successfully
TBL:
13 PETS installed
Up to 21 A current transported
optics understood - no losses
Good agreement current/RF/deceleration
~ 26% deceleration
(Final goal is 40% deceleration)
PETS – Power Extraction & Transfer Structure
More than half a GW of 12 GHz power!
TBL line in CLEX
~ 30 MeV
26%
Measurements at SLAC:
No breakdown last O(8 106 pulses)
-> P consistent with p≤10-7/m/pulse

## Slide 34: Putting it all together: Two-Beam Modules
Maximum stable probe beam acceleration measured: 31 MeV
 Corresponding to a gradient of 145 MV/m
CLIC Nominal, loaded
CLIC Nominal, unloaded
Drive beam ON
Drive beam OFF
Next Steps:
Complete modules being assembled in lab and for beam-tests
Installation and test of full-fledged Two-Beam Modules in CLEX
First module in development, installation end 2013
Three modules in 2014-2016

## Slide 35
Another option for low energies, e.g. 350 GeV:
X-band klystron driven linear collider

## Slide 36
Klystron XL4 series
X-band klystrons (industrialized)
Efficiency
32.5%
18 tubes built to date (not counting rebuilds)
design
performance
CLIC’k klystron:
59 MW
418 kV, 324 A (µK=1.2)
Efficiency 0.436
Klystron XL5 series
CLIC’k klystron:
59 MW
404 kV, 308 A (µK=1.2)
Efficiency 0.474
KMD and X-Band Overview, January 5, 2011 Erik Jongewaard
CLIC’k target
5 tubes have been fabricated at SLAC (1.5 are in operation). The first tube is ordered from industry (CPI)

## Slide 37
PPM, KEK
1994
…A superconducting focusing solenoid system for an X band klystron has been developed. The system consists of a conduction cooled superconducting solenoid, a GM refrigerator and high Tc material current leads. The system cools down to the operation temperature of about 4 K by 4 days just by turning on the refrigerator….
PPM focusing vs. Superconducting Solenoids
In the past 2 decades, the SC technology has progressed a lot. It is worth revising the use of SC (cryogen-free) solenoids for the klystrons again. If cost effective, such an approach will bring benefits for the technology as a whole.

## Slide 38
Scaled (244 ns) 12 GHz DM SLED II performance
CLIC_G
_502
_1
_2
XL5 klystron measured
Klystron peak power for the fixed layout: 2 x Kl(PPM)+PC -> 6 x structures
RF transport efficiency 0.9 is included
Used input: Klystron efficiency 0.55 (measured). Modulator efficiency 0.7 (expected)
Case | CLIC_G | CLIC_502 | #1 | #2
Gradient, MV/m | 100 | 80 | 67 | 57
Length, m | 0.23 | 0.23 | 0.48 | 0.48
P peak, MW | 61.3 | 74.2 | 84 | 76
Efficiency, % | 28.5 | 39.6 | 41.9 | 49.5
F. Merit [a.u.] | 3.81 | 3.3 | 2.79 | 3.41
50 Hz
Designing the linac

## Slide 39
~17.7 m, 16.3 cm
2-pack solid state modulator
59 MW
1.95 s
PPM klystrons
118 MW
1.95 s
492 MW
244 ns
2 m, 1.83 active
x 8 accelerating structures,
100 MV/m loaded gradient
CLIC’k RF unit layout
TE01 900 bend
TE01 transfer line (? m)
Inline RF distribution network
Common vacuum network
460 kV, 2 s flat top
x 4.64
The alternative PC schemes certainly must be considered (especially for the low energy machine), but for our evaluation, we will keep DM SLED II as a base line option, as its performance was confirmed through the high RF power testing.
Compared to NLC, the energy gain per unit in CLIC’k case is 26% lower (need more klystrons per meter), but the unit active length is ~ 2 time shorter.

## Slide 40
Low emittance and luminosity

## Slide 41: Emittance Generation
CLIC @3 TeV would achieve 1/3 of nominal luminosity with ATF performance
(3800nm/15nm@4e9)
Damping ring design is consistent with target performance
Many design issues addressed:
lattice design
dynamic aperture
tolerances
intra-beam scattering
space charge
wigglers
RF system
vacuum
electron cloud
kickers
In addition: wiggler and kicker developments
SSRF

## Slide 42: Main Linac Tolerances
Test of prototype shows
  vertical RMS error of 11μm
  i.e. accuracy is approx. 13.5μm
2) Beam-based alignment
Stabilise quadrupole
O(1nm) @ 1Hz
Pre-align BPMs+quads
accuracy O(10μm) over about 200m
3) Use wake-field monitors accuracy O(3.5μm)
BBA in FACET at SLAC
characterize 500m part
apply orbit correction proc.

## Slide 43: T501: BBA studies at SLAC
T501: FACET test-beam proposal to study advanced global correction schemes for future linear colliders.
CERN-SLAC collaboration where algorithms developed at CERN are tested on the SLAC linac.
The study includes linac system identification, global orbit correction and global dispersion correction.
Successful system identification and global orbit correction has been demonstrated on a test-section of 500 m of the linac.
(Above) Measured Rx response matrix for the test-section of the linac (17 correctors, 48 BPMs)
The section of the SLAC beamlines we work on
(above) Iterations of orbit correction: convergence of the algorithm
(above) Horizontal and Vertical trajectories before and after orbit correction
RESULT: Example of global orbit correction of a test-section of the SLC linac:

## Slide 44: Active Stabilization
 | B10
No stab. | 53%/68%
Current stab. | 108%/13%
Future stab. | 118%/3%
Luminosity achieved/lost [%]
Machine model
Beam-based feedback
Code
Typical quadrupole jitter tolerance O(1nm) in main linac and O(0.1nm) in final doublet
Final Focus QD0 Prototype
Close to/better than target

## Slide 45
A very little bit about detectors

## Slide 46: CLIC Detectors – in brief
Ultra low-mass
vertex detector
with 20 μm pixels
Tracking:
TPC+silicon (CLIC_ILD)
all-silicon (CLIC_SiD)
Fine grained calorimeters for PFA: 1 + 7.5 lint
Strong SC solenoid
4 T or 5 T
Instrumented return yoke
for muon ID
Complex forward region with final beam focusing
6.5 m
Detailed GEANT 4 simulation
Studied using full reconstruction with background

## Slide 47: CLIC machine environment
Drives timing
requirements
for CLIC detector
 | CLIC at 500 GeV | CLIC at 3 TeV
L (cm-2s-1) | 2.3×1034 | 5.9×1034
BX separation | 0.5 ns | 0.5 ns
#BX / train | 354 | 312
Train duration (ns) | 177 | 156
Rep. rate | 50 Hz | 50 Hz
σx / σy (nm) | ≈ 200 / 2.3 | ≈ 45 / 1
σz (μm) | 72 | 44
Beam related background:
Small beam profile at IP leads to very
high E-field
  Beamsstrahlung
    Pair-background
    γγ to hadrons
Simplified view:
Pair background
Design issue
gg → hadrons
Impacts on the physics
Needs suppression in data

## Slide 48: background suppression at CLIC
Full event reconstruction + PFA analysis with background overlaid
  => physics objects with precise pT and cluster time information
  Time corrected for shower development and TOF
Then apply cluster-based timing cuts
  Cuts depend on particle-type, pT and detector region
  Allows to protect high-pT physics objects
Use well-adapted jet clustering algorithms
  Making use of LHC experience (FastJet)
+
tCluster
Triggerless readout of full train
 t0 physics event (offline)
tCluster

## Slide 49: combined pT and timing cuts
1.2 TeV
100 GeV
1.2 TeV background in reconstruction time window
100 GeV background after tight cuts

## Slide 50
The coming years and project implementation

## Slide 51: CLIC physics potential
LHC complementarity at the energy frontier:
How do we build the optimal machine given a physics scenario (partly seen at LHC ?)
Examples highlighted in the CDR:
Higgs physics (SM and non-SM)
Top
SUSY
Higgs strong interactions
New Z’ sector
Contact interactions
Extra dimensions
Detailed studies at 350, 500, 1400,
1500 and 3000 GeV for these processes
Stage 1: ~500 (350) GeV => Higgs and top physics
Stage 2: ~1.5 TeV => ttH, ννHH + New Physics (lower mass scale)
Stage 3: ~3 TeV => New Physics (higher mass scale)

## Slide 52: CLIC Implementation – in stages?
CLIC two-beam scheme compatible with energy staging to provide the optimal machine for a large energy range
Lower energy machine can run most of the time during the construction of the next stage.
Physics results will determine the energies of the stages
3 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
3 km
20.8 km
20.8 km
3 km
48.2 km
Linac 1
Linac 2
Injector
Complex
I.P.
1-2 TeV Stage
0.5 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
4 km
~14 km
4 km
~20-34 km
7.0-14 km
7.0-14 km
Need to operate at
lower than nominal energy

## Slide 53: CLIC near CERN
Tunnel implementations (laser straight)
Central MDI & Interaction Region

## Slide 54: Implementation issues
Physics - how do we build the optimal machine given a physics scenario (partly seen at LHC ?):
Understand the benefits of running close to thresholds versus at highest energy, and distribution of luminosities as function of energy
Construction scenario (and approval scenario):
Explore how we in practice will do the tunneling and productions/installation/movement of parts in a multistage approach ? Environmental impact study
Timescale/lifecycle for project re-defined: Buildup of drive beam (CLIC zero), stage one – physics, more stages/extensions
Parameters: energy steps and scans, inst. and int. luminosities, commissioning and lum. ramp up times.
Power and energy development.
Have started to work on energy estimates (not only max power at max luminosity and the highest energy) based on running scenarios and power on/off/standby estimates
Costs - Initial machine plus energy upgrade: External cost review 21-22.2.2012, costs discussed in volume 3 of the CDR

## Slide 55: Schedule first two stages
year
coord. along collider

## Slide 56: Costs
First to second stage: 4 MCHF/GeV (i.e. initial costs are very significant)
Caveats:
  Uncertainties 20-25%
  Possible savings around 10%
  However – first stage not optimised (work for next phase), parameters largely defined for 3 TeV final stage

## Slide 57: CLIC project time-line

## Slide 58
Not the main line but a growing theme – applying CLIC technology to other projects.
I will now show a few slides on a proton cancer therapy application.
But we try to work more and more with XFELs, Compton sources etc.

## Slide 59
Design project B: cyclinac for single-room proton facility

## Slide 60: TULIP 24 – baseline design
24 MeV
230 MeV

## Slide 61: Backward wave high-gradient accelerating structure for proton acceleration based on CLIC technology

## Slide 62
Thank you for the opportunity to speak and your attention!

## Slide 63
Part 3 – High-gradient physics

## Slide 64
I would like to start this part my presentation with what I believe are some of the essential questions which motivate and direct our study of breakdown – the primary effect which limits the gradient in normal conducting accelerating structrures.
I will then describe some recent progress in answering those questions.
Why bother understanding? Breakdowns happen anyway.
What features on, or near, a surface cause a breakdown to occur at a particular place? How do these features form? What causes the features to begin the run-away process we detect as breakdown? Which leads to the question,
Where does the breakdown rate come from? What gives the principle dependencies – breakdown rate on gradient and pulse length?
Breakdown Physics

## Slide 65
Why bother understanding? Breakdowns happen anyway.
We observe a very strong dependence of achievable accelerating gradient on the rf geometry. Linac parameters are also a strong function of rf geometry: wakefields, shunt impedance, rf to beam efficiency etc.
Being able to predict the gradient a given structure will achieve (based on a specific technology) allows us to optimize the overall design of the accelerator. This dependence is not simply the surface electric field…
Drive Beam Generation Complex
Pklystron, Nklystron, LDBA, …
Main Beam Generation Complex
Pklystron, …
Two-Beam Acceleration Complex
Lmodule, Δstructure, …
Idrive
Edrive
τRF
Nsector
Ncombine
fr
N
nb
ncycle
E0
fr
Parameter Routine
Luminosity, …
Ecms, G, Lstructure
CLIC re-baselining exercise currently underway.

## Slide 66: Maximum surface electric and magnetic fields
Waveguide
damped
Es = 220 - 250 MW/mm2

## Slide 67
High-power design laws
The functions which, along with surface electric and magnetic field (pulsed surface heating), give the high-gradient performance of the structures are:
global power flow
local complex power flow
New local field quantity describing the high gradient limit of accelerating structures.
A. Grudiev, S. Calatroni, W. Wuensch (CERN). 2009. 9 pp.
Published in Phys.Rev.ST Accel.Beams 12 (2009) 102001
Hs/Ea
Es/Ea
Sc/Ea2

## Slide 68
Accelerating gradients achieved in tests.
Status: 4-9-2012
HOM damped

## Slide 69: Power flow related quantities: Sc and P/C
Sc = 4 - 5 MW/mm2
P/C = 2.3 – 2.9 MW/mm

## Slide 70
What features on, or near, a surface cause a breakdown to occur at a particular place?
Our field has depended on the proverbial field emission “tip” with the corresponding field enhancement factor β in order to reconcile observed field emission with the Fowler-Norheim equation.
We keep talking about these tips even though no-one has ever taken pictures of them nor can anyone predict the β a surface will have except through field emission.
Typical values of β in our high gradient accelerating structures are in the range of 50-100.
But there can be more than geometrical field enhancement…
Surface-Emission Studies in a High-Field RF Gun based on Measurements of Field Emission and Schottky-Enabled Photoemission H. Chen, Y. Du, W. Gai, A. Grudiev, J. Hua, W. Huang, J. G. Power, E. E. Wisniewski, W. Wuensch, C. Tang, L. Yan, and Y. You
Phys. Rev. Lett. 109, 204802 – Published 14 November 2012

## Slide 71: Electron emission
Copper surface
typical picture 
geometric perturbations (b)
Fowler Nordheim Law (RF fields):
High field enhancements (b) can field emission.
Low work function (f0) in small areas can cause field emission.
oxides
alternate picture 
material perturbations (f0)
inclusions
peaks
grain
boundaries
cracks
(suggested by Wuensch and colleagues)
(b, f0, Ae, E0)
IFN

## Slide 73: Electrodynamics-molecular dynamic model+ study of a void under tensile stress
ED-MD model follows the evolution of the charged surface.
The dynamics of atom charges follows the shape of electric field distortion on tips on the surface
We also studies the dislocation dynamics on a void burrowed near the surface in Cu held under unilater tensile stress.
Details in F. Djurabekova, S. Parviainen, A. Pohjonen and K. Nordlund, PRE 83, 026704 (2011).
A. Pohjonen, F. Djurabekova, et al., Jour. Appl. Phys. 110, 023509 (2011).

## Slide 74: “Catastrophic”growth of a protrusion at the void
. the top view and a slice of the system at time t = 130 ps when the fully developed protrusion is clearly visible.

## Slide 75: Deformation at realistic electric field strength
Void formation starts at fields > 400 MV/m
Material is plastic only in the vicinity of the defect
Thin slit may be formed by combination of voids or by a layer of fragile impurities
Field enhancement factor ~2.4
Thin material layer over the void acts like a lever, decreasing the pressure needed for protrusion formation
Vahur Zahdin

## Slide 78: DC Spark System Turn on Time
Sample size = 50
The spread in voltage fall times (and current rise times) is extremely small compared to the RF case.
The measured current rise time always shorter than voltage fall time due to initial charging current overlap.

## Slide 79: Summary of turn on times
Test | Frequency | Measurement | Result
Simulation |  |  | 0.25ns
New DC System | DC | Voltage Fall Time | 12-13ns
Swiss FEL (C-Band) | 5.7GHz | Transmitted Power Fall Time | 110 - 140ns
KEK T24 (X-Band) | 12GHz | Transmitted Power Fall Time | 20-40ns
CTF/TBTS TD24 (X-Band) | 12GHz | Transmitted Power Fall Time | 20-40ns
CTF SICA (S-Band) | 3GHz | Transmitted Power | 60-140ns
The turn on time does not seem to be related to the bandwidth of the structures but to the frequency or possibly the intrinsic size.

## Slide 80: Relevant data points of BDR vs Eacc
Steep rise as Eacc, 10 times per 10 MV/m, less steep than T18
TD18
T. Higo, KEK

## Slide 81: TD18_#2 BDR versus width at 100MV/m around 2800hr and at 90MV/m around 3500hr
Similar dependence at 90 and 100 if take usual single pulse?
TD18
T. Higo, KEK

## Slide 82: What are the field emitters? Why do we look for dislocations?
The dislocation motion is strongly bound to the atomic structure of metals. In FCC (face-centered cubic) the dislocation are the most mobile and HCP (hexagonal close-packed) are the hardest for dislocation mobility.
A. Descoeudres, F. Djurabekova, and K. Nordlund, DC Breakdown experiments with
cobalt electrodes, CLIC-Note XXX, 1 (2010).

## Slide 83: Dislocation-based model for electric field dependence
Now to test the relevance of this, we fit the experimental data
The result is:
Power law fit
Stress model fit
[W. Wuensch, public presentation at the CTF3, available online at http://indico.cern.ch/conferenceDisplay.py?confId=8831.] with the model.]

## Slide 84: Pulsed surface heating limit
Cell # (cell #1 is a input matching cell):
4
5
6
7
8
9
10
11
12
13
15
14
17
?16?
Images courtesy of M. Aicheler: http://indico.cern.ch/getFile.py/access?contribId=0&resId=1&materialId=slides&confId=106251
18
Last
regular
cell: 19
It seems that cell #10 (regular cell #9 ~ middle cell) exhibits the level of damage which could be considered as a limit.
A. Grudiev
TD24

## Slide 85
Features in high current region of TD18
Damping waveguide
Inner cell
Current density around 2x108A/cm2 during test

## Slide 86
Electromigration
Our current(!) explaination is that these features are due to electromigration. Electromigration is the transport of atoms in a conductor due to momentum transfer from the current.
This can cause the formation of voids and breakup of the material.
The effect has been a problem in semiconductor interconnects – at current densities of

## Slide 87
MeVArc – Multidisciplinary and multi-application workshop dedicated to breakdown physics
This year 5-7 November – hosted by CERN.
http://indico.cern.ch/conferenceDisplay.py?confId=246618
http://www.regonline.com/builder/site/default.aspx?EventID=1065351

## Slide 88
Thank you for your attention!