## Slide 1: Some information from Nextef
For poster session in IWLC
T. Higo

## Slide 2: Conclusion
Damped structure TD18 was tested
  The BDR seems a little worse than T18.
  Dark current was measured with beta from time to time. Beta X Es seems roughly speaking constant.
Very long-term operations
  BDR decreases but huge time is needed to reach 10-7. Can it be done gradually during operation?
  Need to evaluate the phase shift for this and compare with that of TD18_#3 tested at SAC for much shorter period.
Various findings and issues
  Vacuum pressure gets worse at a few to 10MW level and it is reproducible.
  Double pulse operation was tried. The BDR for each pulse, former and latter, seems the same.
  SEM view was taken and we see gap at the highest magnetic field area. Flatness and bonding jigs may be the issue for improving diffusion bonding.

## Slide 3
T18_Disk_#2
Undamped disk-based
TD18_Disk_#2
Damped disk-based
Strategy
Disk-based
CLIC electric design
KEK mecha design +fab
SLAC assembly
Test at SLAC and KEK

## Slide 4: TD18: Characteristics in vacuum pressure increase at very low power level
VAC-@OUT-WG
VAC@IN-WG
ACC-IN power
Vacuum level was not so good, ~1x10^-6Pa at worst location.
Even after running at top power, the vacuum gets worse when it decreases power.
A few hour stop of RF pulses makes the vacuum level worse in the next startup process, during the recovery passing through the region.
It is reproducible.

## Slide 5
Comparison of dark current
T18_Disk
TD18_Disk
TD18_Quad
Eacc for peak dark current of 10 mA
90MV/m 70MV/m 40MV/m
TD18_Quad
Presented to IPAC10
The amount of the dark current tells the performance of the high gradient breakdown performance!?

## Slide 6
TD18_#2: Evolution of dark current and its spectra
Dark current reduced by three order of magnitude.
It followed roughly modified F-N formula.
b reduced from 70 to 40.
b * Esmax ~ 5~7 GV/m
Averaged Gradient
(MV/m)
MV/m
Electron Energy (MeV)
Peak Current
(nA)
In T18_#2 at 108MV/m, energy peak at 7.5MeV and 3.5MeV, similar to TD18 shown here.

## Slide 7: Breakdown rates in various cutting views
Always changing in this stage of processing, only (? !) a few thousand hours since time=0.
width
Eacc

## Slide 8: Break down rate evolution in TD18_#2
In a short period
Decreasing in a logarithmic time scale BDR ~ t^-0.38
Chart: 
BDR 10^-6 /pulse/m
Chart: 
# BD
Pick up 252 ns
Need too much time to reach 10-7 level.
Cannot wait this long time. Need proper care in fabrication.

## Slide 9
fc-mid, Tr-delay
ramping as time
 building up as time?
252 nsec run
512 nsec run
Little increase vs time!
Different from the left figures.
Need more statistics to judge.
When in the pulse breakdown starts?

## Slide 10: 51+52 BD position
Where in the structure the breakdown happens?
82 BD position
Time difference between Rs and Tr
More to be confident.

## Slide 11: 200ns + 210ns + 200ns
200ns + 50ns + 200ns
Duble pulse operation

## Slide 12: BD timings
Rs delay
Tr delay
Tr delay vs Rs delay
UP delay vs Mid delay
UP delay
Mid delay
Equal probability for BD to happen in former/latter pulse.
Chart: 

## Slide 13: Need better bonding quality!?
Diffusion bonding at high temperature
Need good flatness for the surface to deform within a finite bonding time at high temperature.
Vacuum baking.
Only for surface change. No bonding quality change.
Machining
Brazing
TD18_#3
After high gradient test
SEM taken at CERN
See a gap !?

## Slide 14: Flatness of cells for TD18_#2
TD18_#2_15b
TD18_#2_09b_2
Even ~3 micron flatness was accepted as long as the opposite side was reversely deformed.
Judgment was done by estimating the residual flatness error to be less than 0.5 micron after sandwiching by flat plates.
Mostly potato chip type (right) but one or two cases the conical shape (left) was accepted.