## Slide 1: High gradient studies in simple setups (for discussion)
T. Higo

## Slide 2: Aim and the way to proceed
We want it to complement the tests with CLIC prototype structure evaluation.
It should give us an insight to the basic mechanism.
It should be done in well defined situation.
It should be done in cheap and fast turn around mode.

## Slide 3: Possible RF facilities and their capacities
SLAC
  Single-cell stand 10 tests/yr??
  Pulse heating specific to pulse heating??
  ASTA depends on other programs with high power??
  NLCTA conflict against prototype tests??
KEK
  KT1-B 1 test/month X 8/yr ??
CERN
Others

## Slide 4: What do study ?
Geometry
  (a,t)  C10/CD10
  undamp / heavy damp / DDS / choke
  Quad-like junction
SW / TW
  1-, 3-, 10-cell SW vs 10-cell TW
Es / Hs
  Two-mode

## Slide 5: What do study?
Material
  Impurity
  Inclusion; Ag, Zr, …
  Crystal structure
    Fine Grain, Large Grain
Machining
  Turning
  Milling
    Carbide, diamond, Ra, ball end mill, end mill, ….
  Burr, chamfer, step, rounding, ……

## Slide 6: What do study?
Surface treatment
  HPR or other cleaning such as dry ice
  CP, EP
  Melting by EBW
High temperature treatment
  Vacuum bake
  Hydrogen furnace
  Partial hydrogen gas + vacuum

## Slide 7: How to study with single-cell setup
Need a reference processing protocol
  Valery’s is well established and suitable?
    Without stopping by BD, fast, …..?
  Should be applied to full range of study items
Try to see the processing stage
  Stop and inspect at very early stage
Evaluate at various target levels
  Evaluate such as BDR at medium Eacc=80MV/m? before going to ultimately high level 100—120 and 150-- level

## Slide 8: C10 / CD10
On-going?
How seriously do we proceed now?
Need to evaluate for TW case

## Slide 9: Pulse heating
In-situ time-dependent evaluation
It help us understand the evolution and possibly the key mechanism
Any specific study proposal?

## Slide 10: DC breakdown/FE setup
CERN
Uppsala
SLAC
KEK
Saitama U.
Any comment?

## Slide 11: Coupon surface study
CERN vast study exists in EDMS
SLAC has experience compiled well?
KEK has experience not well documented
Each group does as needed to confirm each technology
Do we need any specific in collaboration?

## Slide 12: Discussion on RF study
Can we confirm vast experimental data taken by Valery’s setup?
Some of them may be worthwhile to restudy.
What can we or should we do in a similar setup but in other view point?
Proposal, comment, ……