## Slide 1: Nextef results ＆ status
International Workshop on Breakdown Science and High Gradient Technology
KEK, Japan
18 April 2012
Toshi Higo

## Slide 2: Contents
Status of Japan and KEK under recovery
Normal conducting X-band studies at KEK
Comparison of four CLIC prototype structures
Undamped prototype T24 result
Damped prototype TD24 result (in operation)
CLIC pulse operation
Effort to identify trigger source leading to suppress breakdowns

## Slide 3: Status of Japan under recovery
One year has passed since 11 March, 2011
  Still frequent earthquakes, but frequency decreasing
East Japan under recovery
  From Tsunami disaster
    Establish to be safe against Tsunami
  Reforming the north-east area
    Assignment as a special area for science
Japan under recovery and reform
  Fukushima nuclear plants
    National trend toward reducing nuclear plants
    Government approval of restarting operation

## Slide 4
Seismic intensity = 6- at Tsukuba on 11 March, 2011
KEK Injector linac at junction between hard and soft
Nextef collapse
due to non-fixed load

## Slide 5
Recent earthquakes in Japan in a week (April 6—13)
We still suffer from frequent earthquakes with seismic intensity of 2~3.
One of the candidate site of ILC in Japan is located in north-east Japan, no big one in several hundred years.

## Slide 6: Status of KEK under recovery
One year has passed since 11 March
KEK facilities were quickly recovered
  J-PARC
  Injector linac
  ATF, STF, Nextef, ……
KEK Tsukuba site strategy
  Recovery budget was approved
  Recovery with reinforcement against earthquakes
  Injector linac is being recovered with various improvement, naturally be suited for SuperKEKB

## Slide 7: Normal conducting X-band studies at KEK
X-band as a main project of KEK until ITRP 2004
  60cm accelerator structure to confirm operation at 65 MV/m unloaded
Continue high gradient as a basic research for accelerator
Join CLIC collaboration
  22cm accelerator structure targeting the operation at 100 MV/m unloaded
Continue and go into a stage
  To identify the trigger of breakdowns and understand initial processing, operation period, later aging, …..
  Studies to improve initial conditioning and nominal performance and to suppress deterioration through operation
The present workshop is one of the step to this end

## Slide 8: Nextef facilities
KT-1
X-band
KT-2
C-band
Nextef
X-band
A
B

## Slide 9
A
B
Control
RF source
Power transfer
Nextef

## Slide 10: Comparison of four CLIC prototype structures

## Slide 11: CLIC test structures; a series of fabrication and test T18 TD18T24TD24
T18_Disk_#2
TD18_Disk_#2
T24_Disk_#3
TD24_Disk_#4
undamped
damped
d
d
2009
2010
2011
2011~12

## Slide 12: SLAC/KEK typical fab/test flow
Design for CLIC (CERN)
Fabrication of parts (KEK)
Bonding (SLAC)
CP (SLAC)
VAC bake (SLAC)
High power test (NLCTA-SLAC)
High power test (Nextef-KEK)
Notes: プロトタイプの試験サイクル
ここでも 日米を基礎におく SLAC・KEK キープレーヤー

## Slide 13: Difference in processing speed among four structures
More BD’s are required for damped!?
Why?
Can it be reduced?
BD’s are essentially needed for processing?
T24
T18
TD18
TD24
Breakdowns are needed or can be avoided?

## Slide 14: Reduced magnetic field 18  24
P (MW), Es (MV/m), Ea (MV/m), DT(C), Sc*50 (MW/mm2)
Iris number
P
Ea
Sc
Es
DT
TD18 unloaded
100MV/m
High Eacc and Es and DT
TD18
Damped
TD24 Damped
Reduce DT
TD24 unloaded
100MV/m
P (MW), Es (MV/m), Ea (MV/m), DT(C), Sc*50 (MW/mm2)
Alexej Grudiev
Notes: TW CLICプロトタイプ 試験 結果
Undamp 100MV/m
Damped → 80MV/m 実現

## Slide 15: Undamped T24
3x10-7
T24 was found much better than T18
Faster processing
Reached low breakdown rate

## Slide 16: Damped TD24#4 at 252ns

## Slide 17: Damped vs undamped
Lines are only for guide for eye and drawn all with the same slope as that of T24 at 40 hr.

## Slide 18
More frequent breakdowns in longer pulse
Not easy to say only from this figure, but longer pulse makes more frequent breakdowns.
Investigate CLIC pulse: effectively shorter pulse.

## Slide 19: Nominal CLIC pulse
F(CLIC)
Rs
Tr

## Slide 20: Only 3 breakdowns in 484 hour operation with CLIC pulse at FLT=100MV/m 1.6x10-7 bpp/m
ACC-IN
Rs
Tr
Rs
F
FC-UP
FC-Mid

## Slide 21: CLIC pulse at 110 MV/m till to date
Operated for 77 hours and encountered 41 ACC-BD.
It results in 1.4X10-5 bpp/m.
BD’s are bunched in time.
BD’s are mostly associated with first-pulse BD’s.
ACC-BD
1st pulse-BD
ACC-IN power

## Slide 22
TD24#4 BDR with CLIC pulse
at FLT=100MV/m

## Slide 23: Single-cell studies in preparation or in mind
Explore basic research in a simple geometry
Center cell is such as the following
  Standard: KEK made – SLAC test
  Nominal: Heavily-damped
  Made of large-grain material
  Undamped but all-milled
  All milled quadrant type
  Choke-mode type
These are under preparation
Notes: 継続申請の3年間の目標 概略
基礎試験の立ち上げ
複合材料を含めた試験
TWでの可能性 見極め
放電頻度を決める放電のトリガーの理解
100MV/m超の加速ユニットの提案

## Slide 24: Basic study setups
High field only at center cell
Clean setup
Crystal characteristics
Damped cell

## Slide 25: Preparation of setup in shield-B
Waveguide
NEG
HEPA
GV
Cavity

## Slide 26: Scanning field emission microscope being under development at KEK
W-Tip
Field emission and surface of crystal characteristics.
Capacitance gauge
Sample
W-Tip
PIEZO actuator
XY stage

## Slide 27: Conclusion
Four CLIC prototype structures have been tested, each for a few thousand hour scale.
Improved performance was given with TD24 type.
CLIC pulse operation met the required BDR for CLIC at FLT=100MV/m.
Basic research area is under construction, expecting to start test in a month or so.
All of KEK members suffer from the huge work for SuperKEKB until the commissioning in 2014.
We want to keep the basic research activity.
We also want to consider a klystron based compact LC for Higgs.
We want to expand X-band based applications, but after SuperKEKB.