## Slide 2: Outline
Introduction
LHC beam is a dangerous beam
LHC Beam Operation /Machine protection
Conclusions

## Slide 3: CERN
CERN Accelerator Complex
Proton Synchrotron
(PS)
Super Proton Synchrotron
(SPS)
Large Hadron Collider
(LHC)

## Slide 4: CERN
CERN Accelerator Complex
CMS
ALICE
ATLAS
LHC-b

## Slide 5
September, 10 2008
Both beams circulating
August 2008
First Injection
LHC milestones
2008
2009
2010
2011
September, 19 2008
Incident
November 29, 2009
Beams back
October 14, 2010
248 bunches
November 2010
Ion run
March 30, 2010
First collisions at 3.5 TeV
LHC timeline
2012
November, 2011
Higgs candidates
July, 2012
5 fb-1
5 fb-1
June, 28 2011
1380 bunches
1380
4 TeV
February, 2012 highest energy

## Slide 6: LHC layout
A schematic view of the 26.7 km-long LHC ring composed of 8 arcs and 8 long straight sections (LSSs)
A two-in-one magnet design, the counter-rotating proton beams circulate in separated vacuum chambers and cross each other only in the experimental interaction regions.

## Slide 7: LHC Parameters
LHC parameters for proton operation 2012
15
6.6

## Slide 8: LHC beam journey
Booster & CPS
SPS injection
SPS extraction
LHC Injection
LHC Ramp
1.4GeV/26 GeV
26 GeV
450 GeV
450 GeV
4 / 7 TeV
Bunch splitting at 1.4 GeV
Single bunch intensity at 26 GeV
Emmittance measurement at 1.4 GeV
Total intensity 2.10 14 /beam
Beam losses end of ramp warning
Luminosity adjustments

## Slide 9
Beams dumped
Pre-injection
flat bottom
Ramp
down
Injection
Filling
Ramp up
STABLE BEAMS
Operating machine
Squeezing
Beams in collision
Collisions

## Slide 10: Cern OP experience
LHC machine operation
  2006 one OP group working in the Cern Control Centre
  Direct line to the Injectors chain (Booster, CPS, SPS)
  Share PPbar and Electron Positron collider experience
‘80 Ppbar beam operation challenge
  Collisions 270 GeV, Intensity P 1013 Pbar 1012
  Old fashion control but already Sequence driven
’90 Electron positron collider dimension challenge
  Injection energy 3.5 GeV, Collisions 45/90 GeV,
  Control software redesigned by Op
2000 LHC PP collider energy & power challenge
  Injection energy 450GeV, Collisions 4/7 TeV
  Intensity 2.10 14
Z particle event in UA1 detector
LEP control room first beam

## Slide 11: Technological Challenges
Stored energy in the magnet circuits is 9 GJ
Stored energy per beam is 360 MJ
Kinetic Energy of 200m Train at 155 km/h
Kinetic Energy of Aircraft Carrier at 50 km/h

## Slide 12: Protection Functions
100x energy of TEVATRON
Beam Dump
Beam Energy
Beam Protection:
0.000005% of beam lost into a magnet = quench
0.005% beam lost into magnet = damage
Failure in protection – complete loss of LHC is possible
8m long absorber Graphite = 800°C
Concrete Shielding
Beam is ‘painted’ diameter 35cm

## Slide 13: Killer beam & downtime
LHC operation is several orders of magnitude more dangerous.
Magnet quench (or a few magnets): a few hours
Collimator replacement: a few days to 2 weeks (including bake out if needed)
Superconducting magnet replacement : 2 months (warming up, cooling down)
Damage to an LHC experiment: many months
Beam accidents could lead to damage of superconducting magnets, and to a release of the energy stored in the magnets (coupled systems)
Experience with the accident in sector 34 in 2008 : one year downtime!!
LHC 50 ns | Intensity x bunch | Nr bunches | Energy [GeV] | Intensity | Energy [MJ] | 
flat bottom PSB | 9.50E+11 | 1 | 0.5 | 9.50E+11 | 0.0001 | x4
flat top PSB | 9.50E+11 | 1 | 1.4 | 9.50E+11 | 0.0002 | x4
flat bottom CPS | 9.50E+11 | 6 | 1.4 | 5.70E+12 | 0.0013 | 
flat top CPS | 1.58E+11 | 36 | 26.0 | 5.70E+12 | 0.0237 | 
flat bottom SPS | 1.58E+11 | 144 | 26.0 | 2.28E+13 | 0.0948 | 
flat top SPS | 1.55E+11 | 144 | 450.0 | 2.23E+13 | 1.6090 | 
flat bottom LHC | 1.52E+11 | 1380 | 450.0 | 2.10E+14 | 15.1389 | x2
flat top LHC | 1.50E+11 | 1380 | 4000.0 | 2.07E+14 | 132.6456 | x2

## Slide 14: When the MPS is not fast enough…
At the SPS the MPS was been ‘assembled’ in stages over the years, but not following a proper failure analysis.
As a consequence the MPS cannot cope with every situation! It is now also covered by the Machine Protection WG but would require new resources…
Here an example from …. 2008 ! The effect of an impact on the vacuum chamber of a 400 GeV beam of 3x1013 p (2 MJ).
Vacuum to atmospheric pressure, Downtime ~ 3 days.

## Slide 15: LHC machine protection Interlock
LHC Beam interlock system
  Interact with all LHC systems involved in the protection of the machine.
  Safe Machine Parameters, Safe Beam Flag, Beam Presence Flag, Mask and Unmasking mechanism
  Interface with the Beam dumping system and the SPS extraction system.
SPS Extraction / LHC Injection Beam interlock system
  Protects the transfer lines from SPS to the LHC.
  Protects the LHC against bad injection.
Software Interlock system
  Detailed surveillance of many machine parameters
Machine Protection Diagnostics
  Detailed post mortem analysis
Remote Base Access Control system
  Token assigned to change parameters

## Slide 16
Safe Machine Parameters
*fast *safe *reliable *available
generates flags & values
afe achine arameters
S
M
P
and / or
directly transmitted
broadcast
receives accelerator information
Injection procedure
protection configuration
Beam Interlocks
Collimation
Beam Loss Monitors …
Extraction Interlocks

## Slide 17
Extraction Interlocks
Transfer Lines
Beam-1 = TT60 + TI2
Beam-2 = TT40 + TI8
Super
Proton
Synchrotron
Large
Hadron
Collider
Extraction Master Beam Interlock Controllers

## Slide 18
Extraction Interlocks
Super
Proton
Synchrotron
Large
Hadron
Collider

## Slide 19
Extraction Interlocks
three beam transfer conditions:
probe
set-up
nominal
Super
Proton
Synchrotron
Large
Hadron
Collider
SPS
Machine
Parameters
LHC
Machine
Parameters
Directly Transmitted
Interlock Signals
Beam presence flag = False Only Safe bean can be injected (1*109)
Beam presence flag = True Any beam can be injected into LHC

## Slide 20: Safe beam flag evolution
Estimated damage level for fast losses
  at 450GeV  ~ 2 · 1012 protons
  at 7 TeV  ~ 1 · 1010 protons
1 · 1012
1 · 109
2 · 1012
1 · 1011
1 · 1010
1 · 108
0.45
2
3
4
5
6
7 TeV
1 · 1013
1 · 1014
1 · 1015
SBF = "True"
SBF = "False"
Energy
I beam
In this intensity range,
a safe beam becomes unsafe
during acceleration
  The Safe Beam Flag depends:
    on the beam energy and intensity
A B D C
Shot | Intensity / p+
A | 1.2×1012
B | 2.4×1012
C | 4.8×1012
D | 7.2×1012
SPS damage by V. Kain Chamonix 2005

## Slide 21: Software interlock
On large accelerators it is not always possible to cover all failure mechanisms with a hardware system:
  It needs something more flexible like adding a new interlock if not too time critical
Survey the control system components relevant for machine protection
  as additional protection layer, with possibility to abort beam if necessary
Provide additional protection for complex but less critical conditions
  (> 12 BPMs over 6 mm for beam 2 horizontal plane (too large RF frequency change)
Threshhold
Trigger orbit excursion >>

## Slide 22: Post Mortem user interface
LHC Post Mortem system is an automated post-operational analysis of transient data recordings from LHC equipment systems
Meant to support machine protection by helping the operations crews and experts in understanding the machine performance and beam dump events and answer fundamental questions:
  What happened? (ie the initiating event / event sequence leading to dump/incident)
  Did the protection systems perform as expected (automated Post operational checks)?
  Assist in trend analysis, statistics of machine performance, …
Each beam dump generates ~ 1GB of PM data which is automatically analysed in typically < 1 min

## Slide 23
Transient data recording after a beam dump (PM)

## Slide 24: Analysis modules for beam PM
RF/ADT data
BBQ/Tune signal
MP3 expert system
COLL hierarchy

## Slide 25: Who’s operating the LHC
LMC LHC machine committee (50)
  Responsible for strategic decision short & long-term
  Highest organ for accelerator technical decisions
LHC Coordinators (6)
  Senior accelerator physicists responsible for the weekly LHC performances
LHC Machine protection committees (6-12)
  Responsible for approval of energy or intensity increase
LHC Engineers In Charge (7)
  Responsible day to day operation when in charge or during his/her special activity.
  All of them
The entire operation team in the control centre is sharing the stressful moments as well as the records achievement

## Slide 26
Since the accident of September 2008 the LHC has been operated at ½ its nominal energy.
In March 2013 the LHC will be stopped for approximately 1 ½ years to perform a complete repair of the defect soldering.
Towards the end of 2014 the LHC will come back online at its full energy for the next adventure of particle physics.
The next's years at LHC

## Slide 27: Summary
LHC Machine Protection Systems have been working well during 2011 run thanks to a lot of loving care and rigor of operation crews and MPS experts.
No quenches with circulating beam.
No evidence of major loopholes or uncovered risks, additional active protection will provide further redundancy.
LHC is a stressfully operation, we are confident on our Machine Protection System which capture most failure before effect on the beam are seen.
We have to remain vigilant to maintain current level of safety of MPS systems while increasing efforts on increasing MPS availability.

## Slide 28: Summary
CERN experiments observe particle consistent with long-sought Higgs boson
“We observe in our data clear signs of a new particle, at the level of 5 sigma, in the mass region around 126 GeV. The outstanding performance of the LHC and ATLAS and the huge efforts of many people have brought us to this exciting stage,” said ATLAS experiment spokesperson Fabiola Gianotti, “but a little more time is needed to prepare these results for publication.”
"The results are preliminary but the 5 sigma signal at around 125 GeV we’re seeing is dramatic. This is indeed a new particle. We know it must be a boson and it’s the heaviest boson ever found,” said CMS experiment spokesperson Joe Incandela. “The implications are very significant and it is precisely for this reason that we must be extremely diligent in all of our studies and cross-checks.”
See you in 2 years with an LHC at 6.5 TeV
Thank you for your attention
Acknowledgement:
Cern op group, Machine protection WG, B.Todd, M.Lamont, J.Wenninger, R.Schmidt, B.Puccio, M.Zerlauth, V.Kain, S.Redaelli, G.Arduini,